## Slide 1
0 0.5 1 1.5 2 2.5 3
3
2.5
2
1.5
1
0.5
0
Heterogeneous Multi-Source Energy Harvesting Interface IC
Tae-Gyun Song1,2, Chan-Hyu Jeon1, Se-Un Shin2, and Hyun-Sik Kim1
1School of Electrical Engineering, KAIST, 2Dept. of Electronics & Electrical Engineering, Dankook University
Conclusion
The proposed dual-energy harvesting I/F IC achieved power extraction FoM of 1,645% and power conversion efficiency of 86.9%. With ultra low power control blocks, the circuit operates on different modes depending on the extractable energy source and supports true cold-startup without previously-charged-energy or battery.
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center (IDEC), Korea.
Proposed Multi-Source Energy-Harvesting Interface Topology
Various Working Modes: depending on the energy source pattern(Piezo or PV or Both) & amount of charged energy
SECE & Energy double pile-up(DPM) are used for Piezoelectric harvesting, and MPPT control optimizes Photovoltaic harvesting
Proposed Dual-Energy Harvesting I/F Chip Architecture
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
1 | Inputted | No | Low (VSTORE < 1.2V)
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
2 | No | Inputted | Low (VSTORE < 1.2V)
VPV > VSTORE
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
1 + 2 | Inputted | Inputted | Low (VSTORE < 1.2V)
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
2 | No | Inputted | Low (VSTORE < 1.2V)
VPV < VSTORE
Passive Energy Harvesting for Cold Startup(Low Energy)
PV Voltage (VPV)
Piezo Voltage (VPL & VPR)
(Temporal Storage) VSTORE
(Main Storage) VOUT
(Startup) SST
Energy Pile-Up Mode
Charged Energy-Level on Super-Cap
Open-circuit voltage sampling for MPPT
Passive FBR for Startup
Async. Boost Converting
Synchronous CoT Boost Converting w/ MPPT
SECE Harvesting
Energy Pile-Up Harvesting
Pile-Up technique virtually increases Piezo voltage and maximizes FoM
Different operations for each working mode are automatically controlled by the internal sensors and pattern recognition block on the chip
PV+Piezo dual-energies are being harvested from the point of cold-start (zero-energy on cap)
VOUT
DPM (16μW)
SECE (~4μW)
FBR (1μW)
x16
Higher
VPZ,OC = 0.6V
FPZ = 140 Hz
x4
DPM
SECE
SECE
FBR
VOUT
VPZ,OC = 1.6V
Shock (0.2s) per 1 sec
VOUT
PCE [%]
Power [μW]
VPV,OC = 0.7V
VOUT
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
3 + 5 | Shock Vibration | Inputted | VSTORE > 1.2V
4 + 5 | Successive Vibration | Inputted | 
PV and Piezo energies can be harvested, simultaneously by time-interleaving for inductor sharing
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
5 | No | Inputted | VSTORE > 1.2V
Synchronous constant on-time (CoT) boost converting operation with MPPT control
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
4 | Successive Vibration | No | VSTORE > 1.2V
Energy pile-up maximizes energy extraction from piezo under successive vibrations
Mode # | Vibration (Piezo) | Solar (PV) | Charged Energy
3 | Shock Vibration | No | VSTORE > 1.2V
SECE: synchronous electric charge extraction
Behaving like a boost converter
SECE is optimized for shock (non periodic) vibration
COUT-CSTORE connection after startup (VSTORE > 1.2V)
Active Energy Harvesting after Startup
Maximized Energy Harvesting
Passive full-bridge rectifier (FBR)
SST works as a diode
For startup: VPL > 1.2V + 0.5V(VD)
PV energy is directly transferred to CSTORE by passive diode
Asynchronous constant on-time (CoT) boost converter using inductor (LIND)
Dual-energy harvesting can be available for cold startup
VOUT
State-of-the-art
This work
Piezoelectric Harvested Output Power [μW]
Piezo-Harvested Output Power [μW] for Shock Vibration
Piezoelectric PCE [%] for Successive Vibration
PV (Solar) Harvested Output Power [μW] & PCE [%]
VOUT
Quiescent Current [nA]
at idle state
Quiescent Current [nA] during Harvesting
Key Operational Waveforms
VOUT
Magnachip/SK-Hynix 180nm CMOS (5mm x 5mm)
Fabricated Prototype Chip
VPZ,OC = 0.6V
FPZ = 140 Hz
Abstract
This study presents a novel Piezoelectric + Photovoltaic(PV) simultaneous dual-energy harvesting interface topology with ultra-low power control circuit. The circuit works in synchronous electric charge extraction(SECE) mode for shock vibrations, and double pile-up(DPM) for successive vibrations to achieve high Piezo energy extraction FoM. To extract PV energy efficiently, MPPT control is adopted. The proposed topology supports a true cold startup which realizes self-powered energy harvesting system. Simulated results showed power extraction FoM of 1,645% and power conversion efficiency(PCE) of 86.9%. The prototype chip was fabricated in 0.18-µm CMOS with 5mm x 5mm active area.
Simulated Results
Prototype chip fabricated in 180-nm CMOS process/ 5mm x 5mm active area
Piezo Energy Harvesting: Max. FoM = 1,645% in DPM with successive vibration, Max. FoM = 460% with shock vibration
PV Energy Harvesting: Peak power conversion efficiency(PCE) = 86.9% @ VOUT = 3V