## Slide 1
Proposed Scheme
Experimental Results
Noise Characteristics of the Charge Sharing Inverter-Based Switched-Capacitor Amplifier
Kiwon Seo, Gunhee Han
School of Integrated Technology, Yonsei University
Conclusion
Abstract
This research presents a new type of switched-capacitor amplifier, which operates without virtual ground and using auto-switched charge sharing . The proposed architecture achieves 13dB and 4dB advanced noise performances at 1Hz and 1KHz compared to the inverter-based switched capacitor amplifier. Proposed and compared amplifiers are fabricated in a 180nm CMOS technology and consuming 12.6uW and 12.4uW from 1.8V supply.
(A) Conventional sc-amplifier Operation
(B) Proposed charge sharing sc-amplifier Operation
Phase 1
Phase 2
Phase 1
Phase 2
<Phase 1>
Difference between and inverter offset is sampled at
is pre-charged to and is pre-charged to
<Phase 2>
Charge of and are shared until
is applied to inverter and turns off the
is fixed to
Noise Power Spectral Density of the Proposed and Inverter-Based SC Amplifier
Chip Photo and Performance Comparison Table
Proposed structure achieves lower noise compared to inverter-based SC amplifier with same power
This structure is effective at lowering the flicker noise of the SC amplifier
In this paper, SC amplifier based on auto-switched charge sharing is proposed. Because of its high output impedance characteristics at the end of the amplification, its noise is relatively smaller than the conventional type of SC amplifier. And we verify that this characteristics is highly effective at flicker noise reduction. This topology can be used at the application which targets the low frequency signal.
2020 IDEC Congress CDC
The chip fabrication and EDA tool were supported by the IC Design Education Center (IDEC), Korea.