## Slide 1
Sensor system consists of sensor, amplifier, filter, ADC and DSP
Conventional transceiver interface has large power consumption and large size
Proposed single signal line, Bi-directional, simultaneous transceiver circuit for wearable sensor system
Communicate 1Mbps sensor data & 250kbps sensor configuration data
Applicable to various signal line lengths
SoC transceiver is implemented in 65nm CMOS process
PPG sensor and transceiver is implemented in 180nm CMOS process
Successfully performed data communication between SoC transceiver chip and PPG sensor & transceiver chip
Single-wire, Bi-Directional, Simultaneous
Interface for Sensor System With PPG Sensor
Jeong-Kyun Kim Dong-Woo Jee
Department of Electrical and Computer Engineering,
Ajou University, Suwon, Korea
dwjee@ajou.ac.kr
II. Proposed System
Conventional System
Required less 4 signal line(MISO, MOSI, SCLK, Select)
Large system size and large EMI noise
Proposed System
Only one signal line for data communication
Small system size, power consumption and noise
Technology scalable system
III. Measurement result
< Fig1. Conventional I/O interface diagram (SPI) >
< Fig2. Proposed transceiver interface for sensor system >
IV. Result
Proposed transceiver system use only single signal line for bi-directional and simultaneous data communication
Data communication is successfully demonstrated between SoC transceiver that is implemented in 65nm CMOS process and PPG sensor and transceiver that is implemented in 180nm CMOS process
Abstract
< Fig5. Proposed transceiver interface chip test setup >
< Fig3. Proposed transceiver interface chip photomicrograph >
< Fig4. Measured results transmitted and received signals >