## Slide 1
Sensor system consists of sensor, amplifier, filter, ADC and DSP
Conventional transceiver interface has large power consumption and large size
Proposed architecture is single signal line, Bi-directional, simultaneous and multi-access transceiver circuit for wearable sensor system
Communicate 1Mbps sensors data & 250kbps sensor configuration data
Applicable to various signal line lengths
Successfully simulated in data communication
Single-wire, Bi-Directional, Simultaneous and Multi-access
Interface Architecture for Sensor System
Jeong-Kyun Kim Dong-Woo Jee
Department of Electrical and Computer Engineering,
Ajou University, Suwon, Korea
dwjee@ajou.ac.kr
II. Proposed System
Conventional System (SPI)
Required less 4 signal line(MISO, MOSI, SCLK, Select)
Large system size and large EMI noise
Conventional System (I2C)
Required only 2 signal line(SDA, SCL)
But large power consumption and low speed limit
Proposed System
Only one signal line for multi sensor data communication
Small system size, low power consumption and low noise
Technology scalable system
III. Measurement result
< Fig1. Conventional I/O interface diagram (SPI) >
< Fig2. Conventional I/O interface diagram (I2C) >
IV. Result
Proposed transceiver system use only single signal line for bi-directional, simultaneous and multi-access data communication
Data communication is successfully demonstrated between SoC transceiver and 4 sensor transceivers
Abstract
< Fig4. Simulated results transmitted and received signals >
< Fig5. Proposed transceiver interface chip test setup >
< Fig3. Proposed transceiver interface chip photomicrograph >