## Slide 1
A Study on Low Power Transceiver for Bluetooth Low Energy 4.2/5.0 Dual Mode Applications
Min Hyuk Lee, Jae Bin Kim, Sang-Gyu Jeon, Tae Young Yoon and Kang-Yoon Lee
Department of Electrical and Computer Engineering, Sungkyunkwan Univ.
jbk0309@skku.edu
Fig 3. shows measured phase noise results of PLL in Rx mode. Bandwidth of PLL is 200kHz.
The frequency offset of Tx and Rx is 1MHz and 2 MHz at the same channel in BLE 4.2 mode and BLE 5.0 mode. The phase noise of Rx mode is -121dBc/Hz at 3 MHz offset.
Fig 4. (a) and (b) show measured phase noise result of PLL of BLE 4.2 mode, BLE 5.0 mode in Tx mode. Bandwidth 1MHz and 2MHz. The value of RMS phase noise of BLE 4.2 mode is 1.749 degree from 1kHz to 1MHz, That of BLE 5.0 mode is 2.382 degree from 1kHz to 2MHz,
Introduction
Proposed Structure
Fig 1. Block diagram of the proposed BLE 4.2/5.0 dual mode transceiver with PMU and SPDT
Architectures of Tx and Rx are analog PLL based on direct modulation instead of IQ up-conversion, and low IF down-conversion.
Tx uses the inductor-less class D type PA for small area and high efficiency.
It requires bandwidth of PLL of 1MHz and 2MHz since PLL based on direct modulation of 1Mbps and 2Mbps.
Low-IF Rx uses a LNTA, a passive quadrature down-conversion mixer, and the TIA that reduce power consumption, a LNTA and 25% duty generation LO are used instead of two LNTAs and normal Lo as in.
Bluetooth low-energy(BLE) standard is a promising wireless connectivity.
Data rate is respectively 1 Mbps and 2 Mbps in the BLE 4.2 and BLE 5.0, the bandwidth of PLL must be sufficiently wide to support the data rate and calibrate accurately .
This paper presents the low power, low-cost RF transceiver that can achieve excellent receiver sensitivity, dynamic range and transmitter spurious performance.
Experimental Result
Fig 2. Measurement board of BLE Transceiver.
Fig 3. Measurement phase noise of the PLL in Rx mode.
Fig 4. Measurement phase noise of the PLL of (a) BLE 4.2 and (b) BLE 5.0 in Tx mode.
(a)
(b)
Conclusion
This paper presents a low power FSK transceiver with integrated SPDT switch and high efficiency power management unit for BLE application.
Power consumption of the receiver and transmitter are 5mW and 6mW from supply voltage of 3V.
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.