## Slide 1
2-Channel DC-DC Converter with Dead Time Controller
for Wearable AMOLED Displays
1. Introduction
Adopting AMOLED display in wearable device is rapidly increasing.
Positive and negative voltages are required to drive AMOLED display.
Body-diode conduction loss due to dead time reduces power efficiency.
2. Circuit Design
Fig 1. Block diagram of proposed DC-DC converter.
3. Results
4. Conclusion
A 2-ch DC-DC converter was designed, channel as the boost converter and channel as the inverting charge pump.
- : 4.6 V , : - 0.6 ~ - 2.3 V.
The dead time controller reduced dead time less than 1 ns.
Adopting the dead time controller, power efficiency was improved by 2.2%.
Tae-Un Kim, Jin-Hui Lee, Seung-Ki Jeon, and Ho-Yong Choi
Department of Semiconductor Engineering, Chungbuk National University
Fig 6. Chip layout.
Item | Summary
Process | 0.18 µm BCDMOS
Input voltage | 2.9 V ~ 4.6 V
Output voltage ( / ) | 4.6 V / -0.6 ~ -2.3 V
Load Current | 1 mA ~ 70 mA
Frequency | 0.15 MHz ~ 1 MHz / 1 MHz
Output ripple | 5mV , < 20mV
Chip size | 1.3 mm X 1.8 mm
Item | Summary
Process | 0.18 µm BCDMOS
Input voltage | 2.9 V ~ 4.6 V
 | 4.6 V / -0.6 ~ -2.3 V
Load Current | 1 mA ~ 70 mA
Frequency | 0.15 MHz ~ 1 MHz / 1 MHz
Output ripple | 5mV , < 20mV
Chip size | 1.3 mm X 1.8 mm
Table 1. Summary of proposed DC-DC converter.
This paper proposes 2-channel DC-DC converter with a dead time controller for wearable AMOLED display to increase power efficiency.
channel is implemented using a SPWM-PWM dual mode boost converter.
Dead time controller
- Lx Level Sensor : Generates a pulse if the dead time does not exist.
- UP/DOWN Counter : Counts the pulse generated by Lx level sensor.
- Delay Circuit : Changes RC delay by varying capacitance according to delay [3:0].
→ Due to dead time controller, the dead time is optimized less than 1ns and
power efficiency was increased by 2.2%.
Fig 5. PSM controller of inverting charge pump.
Fig 4. 0.5X operation of inverting charge pump.
outputs half of boost output voltage using 0.5X inverting charge pump.
PSM controller is consisted of D Flipflop and comparator.
: Control on/off of switching signals. → Reduce power dissipation
Fig 2. (a) Dead time controller, (b) Delay circuit of dead time controller, (c) Switching voltage without dead time controller, (d) Switching voltage with dead time controller, (e) Power efficiency of boost converter
Fig 7. Output voltage and dead time of channel.
Dead time is reduced less than 1ns both under light load and heavy load due to dead time controller.
Fig 8. Power Efficiency.
2.1. - Boost Converter
2.2 - Inverting Charge Pump
(a)
(b)
Gate Driver
Dead time
Controller
SPWM
Controller
S
R
Q
Current
Sensor
+
-
Gate
Driver
Feedback
RC
DIM
Controller
PSM
Controller
Osillartor
DIM[2:0]
GND
GND
(Boost Converter)
(
Inverting
Charge Pump)
Dead time < 1ns
Dead time < 1ns
@ = 3.3 V, =1 mA
@ = 3.3 V, =70 mA
(c)
(e)
The chip fabrication and EDA tool were supported
by the IC Design Education Center(IDEC), Korea.
ISD&T
Integrated Systems Design & Test Lab.
Chungbuk National University
: SPWM-PWM dual mode, Dead time controller
→ Increase power efficiency.
: Inverting charge pump → To reduce area
PSM controller → To reduce power dissipation
(d)
Fig 3. SPWM-PWM controller.
Light load : set-time variable PWM
: set-time varies in proportion to
load current
Heavy load : PWM
: pulse width varies in proportion to
load current
Chart: 
| 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70
with DTC | 39.0453 | 85.3051 | 89.3546 | 93.4131 | 94.581 | 94.2723 | 96.0553 | 95.5503
without DTC | 38.6286 | 84.8791 | 88.5127 | 92.2194 | 93.7466 | 92.9211 | 93.7999 | 94.7247
@ = 3.3, = 4.6 V, = - 2.3 V
Zero Current
Detector