## Slide 1
Dynamic Power Reduction of TCAM Using Selective Precharging of Match Lines
Sung-Yong Kim, Seung-Kwang Hong, and Kee-Won Kwon
College of Information and Communication Engineering, Sungkyunkwan University, Korea
Email: {sykim0819, seung0401, keewkwon}@skku.edu
Analysis of power consumption in TCAM
Power efficient algorithm called Selective Match Line(SML)
More than 50% reduction in power dissipation
Simulation results show 59% power saving on match line
SML has the first 1.5 clock delay and size increase.
Power saving may be different depending on TCAM entry and Search key.
< Fig 1. Concept of SML >
< Fig 4. Timing diagram of SML >
< Fig 3. Architecture of SML >
< Fig 2. Flowchart of SML >
TCAM(Ternary Content Addressable Memory) has the advantage of fast search operation, but it has a disadvantage of high power consumption. Most of this power consumption occurs in the match line, which amounts to 69%.
To reduce this power consumption, we proposed an algorithm called Selective Match line (SML). the operation method of SML only precharges match lines that require operation. Fig 1 shows the concept of SML. It reflects previous search results to select match lines that require action.
Fig. 2 is a flow chart embodying SML. It compares two consecutive search keys to determine which match line is needed for the next search operation, thereby determining precharging of the match line. The comparison of the search key is based on the column where there is no X Cell of the CAM entry.
Fig. 3 shows the structure of SML. Only 'Find X cell module' and 'Search key comparator' are needed in the existing TCAM structure. 'Find X cell module' functions to find X Cell and 'Search key comparator' compares successive search keys to determine precharging.
Fig. 4 shows the timing diagram of SML. Continuous search keys are stored in each register and compared. The result of the comparison determines the signal Comp in the 'Search key comparator'. And the Comp value determines the precharging of the next search cycle.