## Slide 1
Haeyoung Kim, Janghyun Ji, Jinjae Lee, Howon Kim
Department of Electrical Electronic Computer Engineering, Pusan National University
E-mail : ryoung0327@gmail.com, jjh0819@gmail.com, wlswo3149@gmail.com, howonkim@gmail.com
With the recent spread of IoT devices, the unintentional use of vulnerable IoT products is also increasing. The use of vulnerable products continues to increase the number of security breaches, leading to the development of password/authentication SoC security modules to respond to increasing security threats. The use of the SoC security module allows for increased security of vulnerable equipment without replacing existing equipment.
DTLS supporting Crypto Chip(Optimized architecture)
The Design process is digital type and it is Magnachip semiconductor/SK Hynix 180nm process, supply voltage is 3.3V, maximum operating frequency is 100MHz. It is confirmed the operation on the maximum operating frequency of each encryption module is working well and it is highly likely that high speed encryption and authentication will be possible when using this developed encryption/authentication SoC security module.
The cryptographic Core of the SoC security chip is the part that actually encrypts data. It is connected to AXI bus interface for input/output and transmission of data. Dispatcher analyzes command from external interface(SPI, UART) and transmits control signals to the cryptographic cores for processing commands. Every cores are wrapped by AXI Wrapper to make signals for AXI protocol.
<Architecture of Cryptographic Chip>
In this time, we reduced size of HASH module by implementing 16 bit shifted hash calculation. Each round is divided into 4 subrounds. Only 16 bit calculation is performed at each subround and after each subround, data will be 16 bits shifted.
Cryptographic Chip
<Architecture of HASH Module>
AXI
ARIA
GHASH
HASH
ECC
Dispatcher
Data Buffer
Interface
Slave
Slave
Slave
Slave
Slave
Master
SPI, UART
Status
Slave
Interrupt
HASH module is composed of several CSRs(Control and Status Registers) and HASH Core. CSRs store values like key, message, operation code for hash encryption. HASH Core is actual encryption module that calculating hash function.
HASH Core use SHA module for HASH functions. It supports SHA256 and SHA384. Every modules inside of SHA module are controlled by Control Unit. Messages are divided by Word module and divided messages are hashed by compress module. Digest module performs addition at Final round of hash function
a
b
c
d
e
f
g
h
a
b
c
d
e
f
g
h
a
b
c
d
e
f
g
h
subround 1
subround 2
subround 3
a
b
c
d
e
f
g
h
subround 0
<16 bit shifted hash calculations>
SHA module
CU
message
Round
word
const
compress
digest
message
hash_op
round
k
w
hash
length
<Architecture of SHA module>
Scenario | Total Area | Circuit size
100 mhz | 4124020 | 413 kGE
Scenario | Total Area | Circuit size
100 mhz |  | 413 kGE
HASH Module
After synthesis, we got 4124020 total Area size and 413 kGE circuit size.
Results
AXI Slave Wrapper
HASH module
CSRs
CSRs
…
CSRs
HASH Core
SHA module
본 연구는 IDEC에서 MPW를 지원받아 수행하였습니다.