## Slide 1
A Low-Power High-Speed SAR ADC
Sewon Lee and Minjae Lee
Integrated Circuits and Systems Lab.
Gwangju Institute of Science and Technology (GIST)
INTRODUCATION
SAR ADC LAYOUT
Proposed Successive approximation Register(SAR) ADC is aim to have a operating frequency of several tens of MS/s with medium resolution for high speed application such as wireless communication and digital TV.
MEASUREMENT
COMPARATOR
SAR ADC STRUCTURE
Loop Delay
Bootstrap
Comp.
Positive Cap DAC
Negative Cap DAC
CAP DAC
Buffer
CAP DAC
Buffer
SAR Logic
[ Dynamic comparator structure ]
[ Asynchronous SAR ADC structure ]
Adopting asynchronous architecture for achieving low BER.
Reference-less SAR ADC to diminish current consumption.
Three-stage structure enhancing comparator gain.
Reducing input dependent kickback by first stage.
 | This work | [1] | [2]
Technology | 65 nm | 130 nm | 90 nm
Sampling Rate (MS/s) | 30 | 50 | 50
Supply Voltage (V) | 1.2 | 1.2 | 1
Power (mW) | 1.1 | 0.826 | 0.7
Area (mm2) | 0.045 | 0.052 | 0.08
ENOB (bit) | 9.77 | 9.18 | 7.8
FoM (fJ/conv-step) | 42 | 29 | 65
Core ADC occupies 150-um height and 300-um width.
[ SAR ADC Layout ]
[1] C. C. Liu, S. J. Chang, G. Y. Huang, and Y. Z. Lin, “A 10-bit 50-MS/s SAR ADC with a monotonic capacitor switching procedure,” IEEE J. Solid-State Circuits, vol. 45, no. 4, pp. 731–740, Apr. 2010.
[2] J. Craninckx and G. Van der Plas, “A 65 fJ/conversion-step 0-to-50 MS/s 0-to-0.7 mW 9 b charge-sharing SAR ADC in 90 nm digital CMOS,” in IEEE ISSCC Dig. Tech. Papers, Feb. 2007, pp. 24
CAPACITOR LAYOUT
Metal 5 and 6 to minimize the parasitic capacitance.
0.4 fF as a unit capacitor.
[ Capacitor DAC Layout ]
ACKNOWLEDGMENT
The EDA tools were supported by IDEC, Korea