## Slide 1
Bayartulga Ishdorj and Taehui Na
Department of Electronics Engineering, Incheon National University, Incheon 22012, South Korea
The nonvolatile flip-flop (NV-FF) is regarded as a potential substitute for the conventional volatile FF because of advantages such as zero standby power consumption in the standby mode (power saving), instant-ON from power-down conditions (user-experience improvement and power saving), instant-OFF to the standby mode (power-saving and nonrequirement of external NV memory), and prevention of sudden power failure (reliability improvement).
Among the various NV-FF implementations, spin-transfer-torque magnetic tunnel junction (STT-MTJ)-based NV-FFs are considered promising due to their characteristics, including nonvolatility, high endurance, long retention time, CMOS compatibility, scalability, and nil area overhead because of stacking above a MOS transistor.
Recently, it was suggested that offset-cancellation sensing-circuit-based NV-FFs are insensitive to the offset voltage caused by process variation, improving the restore yield. However, these NV-FFs are only valid in the super-threshold voltage region. And are very sensitive to process variations in the near/subthreshold voltage region, because multiple switches for offset-cancellation (Fig. 1.) operation become significant contributors to the offset voltage.
Study on Cross-Coupled-Based Sensing Circuits for Nonvolatile Flip-Flops Operating in Near/Subthreshold Voltage Region
In is study, we investigated two cross-coupled-based sensing circuits for an NV-FF operating in the near/subthreshold voltage region (<0.4 V): a popular cross-coupled inverter-based sensing circuit (CCI-SC), and the proposed cross-coupled NMOS-based sensing circuit (CCN-SC).
We demonstrate that the CCN-SC achieves better restore yield in the near/subthreshold voltage region on the notion that the simplest is the best.
Fig. 3 Simulated restore yield of the state-of-the-art NV-FFs according to VDD. (a) Typical Vth devices are used for PT, NL, NR, and NB. (b) Extremely large devices (10 times larger than the condition in Figure (a)) and low-Vth devices are used for all the transistors.
Fig. 1. Circuit diagram of state-of-the-art NV-FFs. (a) Song’s NV-FF. (b) Na’s NV-FF.
Fig. 4. Simulated transient responses. (a) CCI-SC + DSTA-VLSA. (b) CCN-SC + DSTA-VLSA. The CCN-SC has a higher restore yield than the CCI-SC.
Fig. 6. Simulated restore yield according to the critical transistor width (a) When the RMTJB – RMTJA = 3kΩ. (b) When RMTJB – RMTJA = 1kΩ. When the resistance difference decreases considering MTJ variation the restore yield of CCI-SC decreases drastically. This is because, in the CCN-SC, only the NL/NR Vth mismatch degrades the restore yield, in contrast, the PL/PR Vth mismatch is added in case of CCI-SC. Also, because of the lower IR drop from VDD to ground in the CCN-SC the effective VDD is higher.
Fig. 5. The die photo and structure of the test chip implemented using 65 nm CMOS technology. The structure includes nine 8×8 CCI-SC arrays and 8×8 CCN-SC arrays, each, with different sizes and resistances for yield testing.
Fig. 2. (a) Cross-coupled Inverter (CCI) based Sensing Circuit. (b) Proposed Cross-Coupled-NMOS(CCN) based Sensing-Circuit.
The CCN-SC reduces the number of transistors critical for determining restore yield compared to CCI-SC.
Circuit schematics
Results and Discussion
Test chip
Conclusion
Introduction
Results and Discussion
Table 1: Restore yield and restore failure according to width of the critical transistor when resistance difference value of 1kΩ is assumed.