## Slide 1
D-band CMOS Power Combiner using RF Pad Characteristics
Ui-Gyu Choi°, Dong-Jun Shin, Ji-In Jung, Hyeon-Jin Son, JuHyeon Park, Jong-Ryul Yang*
Electronic engineering, Yeungnam University
E-mail: °ugchoi@yu.ac.kr , *jryang@yu.ac.kr
Background
Conclusion
Methods
Results
Cross Section Of The Proposed Power Combiner.
A Conventional Wilkinson Power Combiner
No additional Calibration required
Chip micrograph of the back-to-back test structure
A power combiner is an important passive device to overcome the limitation of output power in millimeter-wave transmitters.
A Wilkinson power combiner is widely used to combine output power of each power amplifier (PA) with high isolation between two input ports. However, an additional matching network is required in the power combining architecture using the conventional WPC because an output impedance of the PA, which is optimized at a low impedance for increasing output power, should be transformed to the reference impedance.
In this project, a compact and low-loss power combiner which have both the output combining and impedance matching of the transmitter in the D-band is proposed.
A compact size and low loss power combiner using a RF pad characteristics is proposed for the D-band high power transmitter
Measurement Results
This work was supported by NRF grant funded by MSIT (No. 2021R1A2C2004356)
The chip fabrication and EDA tool were partially supported by IDEC, Korea.
< Acknowledge >
Good isolation and asymmetry
Bulky and bandwidth limitation
High loss and skinny line
Works only with 50ohm cells
A Proposed Power Combiner
Proposed Power Combiner Network
Conventional Power Combiner Network
Pad Network
Ideal power combiner isolation simulation
C
C
2RIN
2C
TL1
TL2
TL1
ZIN
ZIN
ZL
G
G
S
M9
M1
Pad MIM capacitor
TSMC 65 nm GP Process 1P9M
Size reduction and low loss by merging the pad network
Zin = 10
Zin = 20
Zin = 50
Area (mm2) | Zin = 10 | Zin = 20 | Zin = 50
w. pad | 0.0375 (0.0093 𝜆02) | 0.035 (0.0087 𝜆02) | 0.038 (0.0096 𝜆02)
w/o pad | 0.012 (0.003 𝜆02) | 0.007 (0.0017 𝜆02) | 0.013 (0.0031 𝜆02)
Zin = 10
Zin = 20
Zin = 50
Minimum Insertion Loss
<Measurement Setup>
<S-parameter Results>
Zin = 10
Zin = 20
Zin = 50
< -0.71 dB
< -0.80 dB
< -1.21 dB