## Slide 1
Design of Low Power Transmitter for Biomedical Application in 180nm CMOS
Dae-Hyeon Kwon, Dong-Hyun Youn and Minkyu Je
School of Electrical Engineering, Korea Advanced Institute of Science and Technology (KAIST)
E-mail: eogus47@kaist.ac.kr
Introduction – Low Power Transmitter for Capsule endoscopy
• High-definition picture should be transmitted outside the person.
• It should be possible to operate for more than 8 hours.
• So, we propose a low power transmitter operating at high data rate ,
and operate more than 8 hours for accurate diagnosis
Chip Implementation
Measurement and Simulation Results
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center (IDEC), Korea.
Overall Architecture of Transmitter
(a) Fractional-N PLL using delta-sigma modulation
(b) 16 QAM constellation and PA core block
(c) Overall block of Ring DCO
(d) Phase noise of the DCO
(e) Layout of transmitter ICs
(d) Measurement setup
• Resolution of TDC required to make the desired frequency is about 20ps
• DCO consists of Start-up, 4 stage ring oscillator with Fine cap. Bank and Coarse current DAC
• Using varactor capacitor, 1 LSB of frequency resolution in fine cap bank is 100KHz
• In some case, even order ring oscillator cannot oscillate , Need Strat-up circuit is required
• The Best insurance is regular Endoscopy
- The surest way to detect stomach and colon cancer
- Recommended once every two years for people over 30 years old
(a) PLL phase noise using code
(b) PLL loop stability using code
(c) PLL phase noise using Simulink
(d) PA amplitude simulation
(e) Measurement of Frequency step of PLL
(f) Phase noise of PLL
TABLE 1. Performance of PLL
• Frequency step of PLL is 140KHz when reference clock is 18MHz.
• Expected value of in-band phase noise in simulation is -105dBc/Hz.
• Measurement value of in-band noise -85dBc/Hz.
• Simulation results differ from measurement results due to timing issue of digital filter
• Advantage of capsule Endoscopy
  We can do the examination painless
  We can maintain daily life while doing endoscopy
  We can diagnose diseases of the small intestine
- Probability of discovery issue
1) Using Conventional endoscopy : < 10%
2) Using Capsule endoscopy : 65 ~75 %
• Circuit Component for transmitter
  Consists of two component
  - Phase-Locked Loops (PLL)
  - Power Amplifier (PA)
  Counter-assisted Fractional N PLL
  - Difficulty of using digital circuit under
  1V supply for low power consumption
  - Can not use DSM for desired frequency
  - Choose PLL without DSM
  - Additionally, No DSM output noise.
  - Good for 16 QAM modulation
  Digital Power Amplifier (DPA)
  - PA is largest power consumption of
  the Transmitter
  - Reduce power consumption as
  reducing circuit that is used in analog
  PA