## Slide 1
A Zero-Crossing-Based Integrator with Bi-directional Two-Phase Charging
Dong-Jick Min* and Jae Hoon Shim
School of Electronic and Electrical Engineering, Kyungpook National University
The integrator uses a new two-phase charging scheme, which is better than conventional two-phase charging schemes in terms of signal-dependent errors, resulting in suppressed harmonic distortions.
The measurements show poor linearity because of some mistakes in the chip design.
 | Post-Sim. | Meas.
Technology (nm) | 28 | 28
Supply voltage (V) | 1 | 1
Signal Bandwidth (kHz) | 196 | 196
Clock Frequency (MHz) | 25 | 25
Oversampling Ratio (OSR) | 64 | 64
Power Consumption (uW) | 188 | 216
Peak SNR (dB) | 75.6 | 69.8
Peak SNDR (dB) | 72.2 | 63.1
Dynamic Rage (dB) |  | 65
The chip fabrication and EDA tools were supported by the IC Design Education Center (IDEC), Korea.
Third-order Delta-Sigma modulator. :Low-distortion feedforward structure.
Half-delay and pseudo-differential zero-crossing-based integrators.
1-bit quantizer & passive adder.
Architecture
Proposed ZCBI circuit.
Error is determined by threshold voltage of M5 ( and gain of inverter ().
.
Circuit Design
Performance Summary
Process
: 28-nm Samsung
: Core Area : 0.3 mm x 0.15 mm
(0.045mm2)
Measurement Result
Power Spectral Density (PSD) Input Amplitude vs. SNDR
Implementation
Conclusion
Acknowledge
The zero-crossing-detector (ZCD) and current source can replace OTA.
The zero-crossing-based integrators (ZCBIs) make signal-dependent error due to the delay of ZCD.
Signal-dependent errors can be suppressed by applying proposed two-phase charging scheme.
Introduction