## Slide 1
Segmented Bit-line based Computation-In-Memory for Energy Efficient Machine Learning Algorithm
Gi-dong Baek and Hanwool Jeong Department of Electronic Engineering, Kwangwoon University
Introduction
Issues of CIM Architecture
Data-intensive하고 Memory access가 많은 머신러닝 알고리즘을 위해 CIM (Computing-In-Memory) 구조가 제안됨.
CIM 구조는 analog signal을 알고리즘의 벡터에 매핑하는데, 이는 회로의 variation에 취약함.
특히 DAC 및 ADC 회로 구조를 사용하고 있는 기존 CIM 구조들[1]-[3]에서 variation으로 인한 SNR 저하가 알고리즘의 추론 정확도까지 저하시키는 것을 확인할 수 있음.
Limited SNR 문제를 해결하기 위해 segmented bit-line을 기반으로 한 charge-sharing CIM 구조를 새롭게 제안함.
Conventional CIM’s Limitation in SNR & Our Proposal
Introduction
Result and Discussion
RBL PCH를 통해 input vector를 구현하고, weight vector는 각 subarray에서 bitcell에 1-bit 형태로 저장함.
Segmented RBL의 capacitance와 RBL PCH 및 RBL Buffer를 이용해 multi-bit precision을 갖는 vector multiplication을 구현함.
Proposed CIM Architecture with Segmented Read Bit-line (RBL)
Simulation Results
제안한 CIM 구조는 variation에 취약한 기존 구조의 단점을 segmented bit-line을 이용한 charge-sharing operation으로 robustness to variation을 갖는 구조임.
제안한 구조는 65nm 공정에서 설계 되었으며, 16μm2의 Area를 차지함.
제안한 구조는 500 MHz의 frequency로 동작되며, 1.2V의 supply voltage 하에 구동됨.
Conclusion
[1] J. Zhang, Z. Wang, and N. Verma, "In-Memory Computation of a Machine-Learning Classifier in a Standard 6T SRAM Array," IEEE Journal of Solid-State Circuits, vol. 52, no. 4, pp. 915-924, 2017.
[2] A. Biswas and A. P. Chandrakasan, "CONV-SRAM: An Energy-Efficient SRAM With In-Memory Dot-Product Computation for Low-Power Convolutional Neural Networks," IEEE Journal of Solid-State Circuits, vol. 54, no. 1, pp. 217-230, 2019.
[3] S. K. Gonugondla, M. Kang, and N. Shanbhag, "A 42pJ/decision 3.12TOPS/W robust in-memory machine learning classifier with on-chip training," in 2018 IEEE International Solid - State Circuits Conference - (ISSCC), 2018, pp. 490-492.
Reference
Operational waveforms of RBL precharge circuit.
Operational waveforms of RBL buffer for developing RBL to .
(a)
(b)
(a) Operational waveforms of the CIM for precharge operation and (b) the precharged BL distribution comparison of the proposed CIM and the structure of [2].