## Slide 1
Fully Integrated Triple-Mode Ka-Band Power Amplifier with
Vertical-Horizontal Combined Transformer for 5G NR Applications
Geuntae Kim, Kyutaek Oh, and Ockgoo Lee
Department of Electrical Engineering, Pusan National University
Introduction
CMOS PAs for NR 5G mm-wave applications
  High-order QAM, large BW with large PAPR -> Large back-off from PSAT
High POUT with compact parallel power combining transformer at mm-wave region
  Multiple combining, low loss, compact area
Triple mode operation → Increasing efficiency in back-off region
Extending the battery usage of portable device
The chip fabrication and CAD tools were supported by the IDEC, Korea.
Simulated Result
Proposed PA using Vertical-Horizontal combined transformer
Conclusion
Vertical-Horizontal combined transformer is proposed → Compact die area, Multi-mode operation
  Designed mm-wave multi-mode CMOS PA
  High PSAT: 23.5 dBm with 41.5% PAE, High gain: 28.5 dB
  High PAE in back-off region
  → PAE at 5-dB back-off : 21.5%, 10-dB back-off : 13%
[Chip Layout of the designed PA, Size : 0.49 mm2]
[Proposed Vertical-Horizontal Combined transformer]
  Vertical-Horizontal combined configuration -> Compact size (145 μm 66 μm)
  Low current consumption in back-off region(MP & LP modes)
  Improvement current consumption at 5-dB back-off : 27.1%, 10-dB back-off : 61.1%
[Schematic of the proposed Triple-Mode CMOS PA]
[S-parameter]
[Gain & PAE vs. output power]
[Stability Factor]
[Current Consumption of PA]
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
(65nm CMOS process)