## Slide 1
A 0.7V Nano-Power Dynamic Voltage Reference for IoT Applications
Heungsik Eum and Youngcheol Chae Department of Electrical and Electronic Engineering,
Yonsei University, Seoul, Korea
Trimming Method
Conclusion
CTAT generated by CMOS-based discharge (exponential region)
independent on initial voltage ()
Auto-zeroing Long-hold Buffer
Voltage reference for IoT applications should have low-power consumption & small area occupation
Better * TC & LS both are required in voltage reference for IoT applications (<100nW)
Reference voltage should be buffered for measurements
Offset cancelation by auto-zeroing
Bulk-source connection & buffer block bulk leakages
Motivation
Dynamic Reference
Power consumption vs Area
Performances of Reference
* TC: Temperature Coefficient [ppm/]
LS: Line Sensitivity [%/V]
Zero-TC generated at optimal time ()
Controllable optimal time by size ratio
Reference voltage determined by difference of threshold voltage
Trimming by time ()
Time-controlled trimming doesn’t cause additional errors (simple)
One-point trim reduces inaccuracy from 1.2% to 0.3%
,
Simulation Results
Better performance of TC (<13.6ppm/) and LS (<0.137%)
Low-supply & low-power operation
CMOS-based Discharge
Proposed