## Slide 1
A Resistorless Low-Dropout Regulator with Low Power Voltage Reference based on Subthreshold MOSFET
Hyoung-Jun Na, Tae-seob Oh Jae-bin Kim, Jong-wan Jo and Kang-yoon Lee School of Electronic and Electrical Engineering, Sungkyunkwan University, Suwon, 16419, Korea E-mail : why9887@g.skku.edu , souliu@skku.edu, jbk0309@skku.edu, jw1114@skku.edu, klee@skku.edu
IC Lab(IC Lab)
[1] Y. Osaki, T. Hirose, N. Kuroki and M. Numa, "1.2-V Supply, 100-nW, 1.09-V
Bandgap and 0.7-V Supply, 52.5-nW, 0.55-V Sub bandgap Reference
Circuits for Nano watt CMOS LSIs," in IEEE Journal of Solid-State Circuits,
vol. 48, no. 6, pp. 1530-1538, June 2013.
[2] Behzad Razavi, “Design of Analog CMOS Integrated Circuits, Second
Edition”, Mc Graw Hill Education, 2015.
[3] H. Zhang et al., "A Nano-Watt MOS-Only Voltage Reference with High-Slope
PTAT Voltage Generators," in IEEE Transactions on Circuits and Systems II:
Express Briefs, vol. 65, no. 1, pp. 1-5, Jan. 2018.
[4] S. B. Nasir, S. Sen and A. Raychowdhury, "Switched-Mode-Control Based
Hybrid LDO for Fine-Grain Power Management of Digital Load Circuits," in
IEEE Journal of Solid-State Circuits, vol. 53, no. 2, pp. 569-581, Feb. 2018.
References
Fig 2. Architecture of low power MOSFET voltage reference
Introduction
The curvature-compensated CMOS BGR (Band-Gap voltage reference) and Low-Drop Voltage Regulator circuit implemented with only MOSFET transistors operating from 1.8V to 3.6V. In an ultra-low power BGR (ULP), a high-slope PTAT (Proportional-to-Absolute Temperature) voltage generator and nano-ampere current reference are used as bias circuits and Complementary-to-Absolute Temperature (CTAT) voltages. In the proposed structure, only one PTAT stage is used to compensate the CTAT voltage directly generated by the diode-connected NMOS in the current reference circuit
Block Schematic Architecture
Fig1. Block diagram of the low-power circuits architecture
Fig 4. Architecture of resistorless LDO based on subthreshold MOSFET
Conclusion
This structure is designed in the sub-threshold region and consumes 747 nW of power for an input voltage of 3.3V. Measurements show a -55dB PSRR, a TC of 16 ppm/°C within the range of -40°C to 80°C, and a line regulation of 7.6 mV/V for supply voltage variation of 1.8 V to 3.6 V
Experimental Results
Table 1. Performance Comparison with other works
Supply Voltage | 1.8V ~ 3.6V
Output Voltage | 12V
Line Regulation | 7.6 mV/V
Load Regulation | 0.73mV/mA
TC | 16ppm/℃
PSRR | -22.5dB@190kHz
Power Consumption | 747 nW @3.3V
Die area | 195 um * 390 um
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Fig 3. Architecture of nano-Ampere current reference