## Slide 1
Infrared camera configuration
Proposed readout integrated circuit system
▪ nine (3 × 3 array) microbolometers share one unit circuit. ▪ The size of the entire array is 1026×768, and the unit circuit has an array of 342×256. ▪ Temp. sensor: To detect substrate temperature. ▪ Dark sensor: To obtain the reference value of a dark current. ▪ Suppression circuit: controls the bias and dark current of the microbolometer.
Proposed Pixel-Level ADC
▪ Integrator, A1
- Time division integration for 2.21ms.
- Integration of sensor current IS and DAC output.
▪ Comparator, A2
- CDS for suppressing low-frequency noise.
- Comparing the output of the integrator with the reference (VB2).
▪ Using the Sequential Method
- Enable efficient use of time and guarantee sufficient integration
time.
▪ Using the Time-to-Digital Method
- Perform integration and A/D conversion simultaneously.
- Valid information on the saturated voltage before the maximum
integration time can be obtained, so the operating range is wide.
Measured Waveforms
▪ Control signal
- SEL_C : resend VCM.
- RST : comparator reset.
- HOLD : Integrate the current signal IS.
- L : Activate the comparator.
- RAMP : Supply a signal in the form of a ramp.
▪ Large current signal : IS2
- Stop comparing with VTH and compare with VSAT.
- When the comparison with VSAT is completed, the comparison
is completed as soon as it is saturated.
▪ Small current signal : IS3
- the integral signal does not reach VSAT.
- a Ramp-type VSAT is used to enable comparison for small current input.
▪ Sequential time-to-digital ADC
- All signals are shifted for sequential operation.
- By shifting the signals, the VCM delivery time and integration start
time were sequentially operated in row units.
Comparison
Conclusion Summary
Mask layout & pixel array
To design a signal acquisition circuit for a high-resolution microbolometer, a high precision bias suppression
circuit and a sequential time-to-digital ADC in pixel units were proposed. The proposed signal acquisition circuit is suitable for System-on-Chip
applications that require an infrared detection system and provides excellent infrared image quality by guaranteeing a wide operating range and high SNR for infrared detection signals.
This work was supported by the IDEC (IC Design Education Center) of KAIST.
Schematic diagram of the proposed ADC
Timing diagram of the proposed ADC
▪ DB Hitek 180nm BCDMOS
▪ Size of the array: 1026 x 768
▪ Size of unit pixel: 15 m x 15 m
▪Infrared cameras are attracting attention as a solution for self-driving cars because they can identify objects even under conditions that are difficult to identify with the eyes.
▪Demand for small and low-power infrared cameras is increasing as demand for smart homes, IOTs, and wearable devices increases.
▪Improving image quality with small size and low power requires a wide dynamic range and a high signal-to-noise ratio.
2023 IDEC Congress(CDC)
Row Counter
13-bit ADC/DAC
Suppression circuit
Dark sensor
Temp. sensor
Timing circuit
‘33’
array
Unit cell
circuit
342256 ‘33’
array
Row scan
Column multiplexer
Reference signal generator
Parameter | Value
Detector pitch | 15 μm  15 μm
Resistance | 10 MΩ
Thermal conductance | 0.7 × 10-8 W/K
Emissivity | 80 %
TCR | 2.5 %
Frame rate | 50 Hz
Bias current(IB) | 40 – 120 nA
Signal current(ISIG) | 0 – 8.8 nA
Maximum integration time(tINT.MAX) | 1.95 ms
Integration capacitor(CINT) | 1 pF
Power consumption | < ?? μm/pixel
 | Dynamic range [dB]
(A) | 65.5
(B) | 56.2
(C) | 80.9
A1
VB1
RST
CINT
S
CCDS
cds switch
A2
VB2
VY
Level
Shifter
Detector
Power control
Vrst
Vth2
Vsat
Vramp
13-bit
SRAM
write
Switch control
13-bit Counter
IB
3  3
sensor
CM
VCM
 SEL_C
IS
HOLD
Unit cell ( pixel array) circuit
S
Column multiplexer
DAC
Mp2
Mp1
Mp3
Mps
RBB
Mp4
RST
Vth_L_active
Vth_H_active
Ramp_active
A1
VB1
RST
CINT
A2
VB2
RST
CM
VCM
 DAC
IS
HOLD
DAC
IB
S
IB+ IS
Vps
Mp3
Mps
RBB
Mp1
Mp2
High Precision Bias Suppression
▪ In the case of a general microvolometer, the bias current is larger than the signal current.
▪ The High Precision Bias Suppression circuit is used to remove the bias current.
▪ Ensure sufficient integration time with a limited integration capacitor.
▪ Activate the switch to enable the feedback circuit for amplifiers and .
▪ Determine , which serves as a variable resistor on , to remove the bias current for each pixel.
Unit circuit for typical Single Slope ADC
Switch Control Signal for Time-to-Digital variable clock operation
Shift operation for variable clock
Pixel Level Sequential Time-to-Digital ADC with Wide Dynamic Range
and High SNR for High-Resolution Microbolometer FPA
Jong-Beom Kim, Eun-Ji Won, Doo-Hyung Woo
School of Information, Communications and Electronics Engineering The Catholic University of Korea
Introduction
Proposed readout circuit
Experiment result
Time
VRST
VSAT
V(CINT)
Tmax
T
2T
T
T
RST
Hold
Vth_L_active
Vth_H_active
Ramp_active
SEL_C
Vth2
Vth1
Integration & ADC
Readout
(0.15 ms)
Maximum integration time (1.95 ms)
1/9 frame (2.2 ms)
Vramp
…
I1
I2
I3
T`max
T`max_end
IS[1] integration & 13-bit Time-to-Digital ADC
R/O[1]
R/O[2]
R/O[3]
…
6 s
IS[2] integration & 13-bit Time-to-Digital ADC
IS[3] integration & 13-bit Time-to-Digital ADC
1/9 frame (2.22 ms)
4 s
IS[256] integration & 13-bit Time-to-Digital ADC
2.21 ms
VCM[1] update
VCM[2] update
VCM[3] update
VCM[256] update
…
IS[1] integration&ADC
R/O[1]
6 s
1/9 frame (2.22 ms)
VCM[1] update
IS[2] integration&ADC
…
1.54ms
IS[3] integration&ADC
IS[256] integration&ADC
R/O[2]
0.48ms
…
0.2ms
VCM[2] update
VCM[3] update
R/O[3]
R/O[256]
VCM[256] update
IS[1] integration
13-bit SS ADC[1]
R/O[1]
R/O[2]
…
…
6 s
IS[2] integration
1/9 frame (2.22 ms)
4 s
13-bit SS ADC[2]
IS[256] integration
1.96 ms
0.25 ms
VCM[1] update
VCM[2] update
VCM[256] update
R/O[3]
IS[3] integration
13-bit SS ADC[3]
VCM[3] update
integration and 13-bit A/D conversion
Common single slope ADC
Sequential Single Slope ADC
Proposed Sequential Single Slope ADC