## Slide 1
Design of NRZ/PAM-3 Multi-mode Transmitter for Next-generation Memory Interfaces
Byung-Du Choi and Joo-Hyung Chae
Electronics and Communications Engineering, Kwangwoon University
Introduction
Data rate per pin in memory interfaces is continuously increasing.
PAM-4 signaling is a new candidate, but it has a limitation in single-ended signaling owing to reduced SNR.
PAM-3 signaling can be an alternative.
To support backward compatibility, NRZ/PAM-3 multi-mode is required.
NRZ/PAM-3 transmitter consists of PRBS generator, PAM3 encoder, mode controller, 2:1 serializer, and driver.
According to the operation mode, the mode controller adjusts the data transfer path.
PAM-3 encoder performs 3-bit/2UI encoding, leading to a 1.5x data rate.
Output driver can support both NRZ and PAM-3 signalings.
Prototype was fabricated using a 65-nm CMOS process.
Using a 4GHz clock signal, a prototype chip for NRZ/PAM-3 transmitter was measured.
8-Gb/s data rate was achieved for NRZ mode.
12-Gb/s data rate was achieved for PAM-3 mode because PAM-3 signaling can transfer 1.5x data compared to NRZ signaling.
PAM-3 can be a promising signaling for next-generation memory interfaces.
NRZ/PAM-3 dual-mode transmitter was implemented and proved.
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Memory Interface Trends
NRZ
PAM-4
PAM-3
1.5x Data Rate
Improved SNR
Overall Architecture
NRZ Mode
PAM-3 Mode
Measurement Results
NRZ (8Gb/s)
PAM-3 (12Gb/s)
1bit/1UI
3bit/2UI
Conclusion and Acknowledgement
Process | 65 nm CMOS
Signaling | Single-ended Dual-mode PAM-3/NRZ
Clocking Architecture | Half-rate
Supply | 1.0 V
Data-rate/Pin | 8 Gb/s (NRZ) 12 Gb/s (PAM-3)
< Performance Summary >