## Slide 1
Enhancing Performance and Reliability of eDRAM
with Pre-Amplifier-Based Sense Amplifier and BIST
Introduction
Challenges of eDRAM Implementation
  Insufficient sensing margin due to high parasitic-to-cell cap. ratio
  High Cost at Reliability Testing
Chip Photo, Measurement and Future Plan
Overall Architecture
BIST Logic for eDRAM
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Acknowledgement
Donghwan Kim*, Gi-Woo Lee* and SeongHwan Cho
Department of Electrical Engineering, KAIST, Daejeon, Korea
Enlarges sensing margin using high gain of pre-AMP
Sense Amplifier with Pre-amplifier
Built-In Self Test(BIST) Logic for eDRAM
Reduces the testing cost using 5 adjustable modes
Contributions and Scope of the Work
Implemented with TSMC 65nm Technology(HM-2201)
  256x256 cell array with 256 SAs
  Effective area: 0.61
Future Plan
  Auto-zeroing technique can relieve the mismatch effects
5 BIST Modes
- RESET
- PRESET
- NORMAL
- RETENTION(RET)
- Sequential Check(SQC)
Large Variation of Pre-Amplifier due to Offset Mismatch
Sensing Margin Relationship w/ respect to # of WLs
State Machine of BIST Modes
Analysis
The offset of Pre-AMP is amplified by CP/C0(1st AMP)
The offset variation of AMP should be minimized
Chip Photo
Measurement Set-up
Measurement of Pre-AMP Over Multiple Chips
Expensive Cost for DRAM Reliability Testing
  The five individual modes are designed to automatically produce their respective outputs, thus reducing the testing cost significantly
Verification of BIST Logic through Simulation
Verification of Two Modes(RET and SQC)
62mV
Large Mismatch
(370mV variation)
Meas. #1
Meas. #2
VOUT1(V)
VOUT2(V)
0.6
0.2
1
0.2
0.6
1
1st AMP large Mismatch
VIN1(V)
VIN2(V)
Implementation of eDRAM Macro
Overall Architecture of eDRAM Macro
Sense Amplifier with Pre-Amplifier
Among the 256 bits from the memory MAT, the 16 bits selected by the column decoder are sent to the chip's external interface and the BIST block.
Configuration and the operation of the proposed Sense Amplifier
The preamplifier consists of two stages in total. The first stage adopts a folded cascode structure to achieve high gain.
By the operation of switched capacitor amplifiers, it is possible to convert the charge stored in the cell directly into voltage without any charge sharing.
Bad Sensing Margin
Sensing Failure