## Slide 1
A Variable Gain Active Phase Shifter for D-band
with Low RMS Phase and Gain Errors
Yeonseung Kim and Songcheol Hong
School of Electrical Engineering, KAIST, Daejeon, Republic of Korea
Introduction
Chip Implementation and Measurement Results
Conclusions
Schematic Design
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
[ Attenuation factor in air ]
[ Phased array structure ]
Advantage of D-band frequency
Low attenuation factor in air
Small area for phased array configuration (antenna distance ≈ 1/frequency)
Phase shifter is key-block for phased array
The RMS error of a phase shifter has a direct impact on the accuracy of the beam pattern of a phased array structure
 Low RMS error is important
Chip photograph
IQ generator simulation results
Proposed phase shifter
Gilbert-cell based active phase shifter structure [1]
Hybrid coupler type IQ generator used
Phase(8bit), Gain(6bit) controlled by DAC
Short-channel transistor current source is used to cancel the channel length modulation effect [2]
Inter-stage VGA used for reduce IQ error
[1] JSSC – 0.13𝜇m CMOS phase shifters for X-,Ku-, and K-band phased arrays
[2] TCAS-‖ – A W-band vector modulator using short-channel transistor current sources and impedance compensation varactors
Gain control DAC
Phase control
DAC (+)
Phase control
DAC (-)
Phase / gain control DAC schematic
IQ generator layout
Hybrid coupler type IQ generator is optimized at 144 GHz.
The loss characteristic is -2 dB (ideal distribution loss 3 dB is excluded)
The phase difference characteristic is 87˚ (3˚ phase error)
Measurement set-up
Vector control states of proposed phase shifter is measured by Keysight PNA (N-5247B) with D-band extender (N5262BW06-STD) and D-band Cascade probe tip
Chip area : 0.9
Measurement results
(a) Return loss
(b) Insertion loss
(c) Constellation – all bit
(phase-8bit / gain-6bit)
(d) Constellation - LUT
(phase-6bit / gain-4bit)
(e) Constellation - LUT
(phase-5bit / gain-3bit)
Return loss : S11<-5dB / S22<-10dB (in D-band)
Minimum insertion loss : -13 dB (@150 GHz)
All phase and gain bits at 150GHz in Figure (c) are used to make the target vector by using the look-up-table (LUT) generation method [3]. The LUT generation results of phase-6bit, gain-4bit in Figure (d), and phase-5bit, gain-3bit in Figure (e).
RMS errors : (d) – phase:0.98˚,gain:0.145dB / (e) – phase:1.01˚,gain:0.15dB
[3] MWCL – A 60-GHz polar vector modulator with lookup table-based calibration
Comparison table
* Best value in given frequency band
A D-band variable gain phase shifter with low RMS phase and gain errors was implemented and verified. The proposed phase shifter has 6bit-phase and 4-bit gain controls with 2-bit calibration each. The phase shifter has 0.98˚ RMS phase error and 0.145 dB RMS gain error with these control bits. Especially compared with the D-band phase shifters, as in the comparison table, this work shows less RMS errors.
Proposed phase shifter schematic
Proposed phase shifter block diagram
Vector summer input impedance varies during vector control because vector summer MOSFET (M7-M14) operation region varies from off-state to saturation region, and if vector summer is directly connected to the quadrature generator, this variation induces the IQ error in the quadrature generator
 Inter-stage VGA reduces IQ errors by preventing the effect of vector summer input
impedance change on the quadrature generator.
The commonly provided MOSFET modeling of the D-band is not accurate. This inaccuracy mainly effect the IQ gain error
 Inter-stage VGA adjust each IQ path gain for reducing IQ gain mismatch
Advantage of inter-stage VGA