## Slide 1
A 8GHz Phase interpolator based on charge pump with 0.23% Phase Error
Hyunsu Jang, Jongchan An, Gwangmyeong An, Yoonsang Lee, Geungbae Kim, Jinsoo Bae, Junyoung Song*
Dept. of Electronics Engineering, Incheon National University, Incheon, South Korea
■Phase interpolators are widely used in digital communication systems for generating intermediate phase signals between two input signals.
■ The inherent issue of a PI operating in current mode is the substantial current consumption by the PI.
■ The conventional PI using an inverter results in a significant power consumption.
1. Background
2. Proposed Design
3. System Architecture & Simulation Results
■Simulation results demonstrate that without the application of these techniques, the current mismatch ranges from 14uA to 134uA, whereas with the application of both techniques, the mismatch is significantly reduced to a range of 52nA to 61nA. This enhances the precision of interpolation.
■ The utilization of a charge pump-based PI enabled achieving a phase error of 0.23% at low power consumption.
Acknowledgement The chip fabrication was supported by the IC Design Education Center(IDEC), Korea.
Reference [1] Bruno W. Garlepp, et al, "A Portable Digital DLL for High-Speed CMOS Interface Circuits," in IEEE Journal of Solid-State Circuits, vol. 34, no. 5, May.1999.
[2] B.Razavi, "Design of Analog CMOS Integrated Circuits, Second Edition, " Mc Graw Hill Education, 1999.
[3] Aravind Tharayil Narayanan, et al, "A Fractional-N Sub-Sampling PLL using a Pipelined Phase-Interpolator With an FoM of -250dB," in IEEE Journal of Solid-state
Circuits, vol. 51, no. 7, July. 2016.
4. Conclusion
■ In order to facilitate the charging and discharging operations of the charge pump, an 8GHz clock is provided as the input to the switches.
■ Dynamic biasing adjusts the gate voltage to bias the PMOS and NMOS current sources in such a way that the current mismatch between them is minimized.
■ Bootstrapping reduces current mismatch through pre-charging, resulting in improved accuracy of interpolation.
TOP architecture of proposed design
Schematic of the proposed Charge pump
Simulation result that is the current mismatch as a function of Vout
Transient simulation