## Slide 1
A Ternary Neural Network Computing-In-Memory Processor with 16T1C Bitcell Architecture
Hoichang Jeong, Seungbin Kim, Keonhee Park, Jueun Jung, and Kyuho Lee
Ulsan National Institute of Science and Technology
Motivations
Experimental Results
Key Features of Ternary-CIM
<Necessity of Computing-In-Memory>
Energy consumption in memory access 
Computation delay in memory bottlenecks 
Processor-memory performance gap 
  CPU speed: 55% increase per year
  DRAM speed: 7% increase per year
 Computing-In-Memory (CIM), an "ALU-memory integrated architecture" for low energy 
< Disadvantages and Improvements of Charge-domain CIM >
Charge-domain CIM
  Require extra area for capacitor 
  ADC power overhead 
Proposed Ternary-CIM
  No additional area by using MOMCAP 
  ADC Less Design 
<16T1C Ternary Bitcell with Ternary Multiplication>
Multiplication in 16T1C Ternary Bitcell (MULT)
16T1C Ternary Bitcell : 2×6T SRAM cell + 4T computation logic + 1 computation capacitor (MOMCAP)
Ternary weight is stored in 2 SRAM cells
  Left cell: MSB / right cell: LSB
Ternary activation is connected to source and drain of 4T computation logic
Ternary MULT is shown in 1 computation capacitor
<Column-wise Inter-bank Ternary MAC w/ Decision Thresholding>
Add between Ternary Bitcell (ADD/ACC)
  Column-wise MAC computation
Computation logic of Ternary Bitcells in single column is linked to each other to compute
Weakness of charge-domain operation
  Slow pull-up due to NMOS 
  Long MAC operation time (10 ns) 
Decision thresholding
  Decision thresholding voltage (0.5 mV), Decision thresholding time (3.0 ns) set
  70% less computation time than SOTA 
<Charge-based Psum Adder & Flexible Data Mapping Strategy>
Charge-based Psum Adder (CPA)
  ADC-less Psum computation
  [-1,152,+1,152] ↔ [65 mV, 585 mV]
Flexible Data Mapping
  Pipeling between 4 TBA & 4 CPAs
  Perform layer (CONV/FC) in TNN
TNN acceleration with 56x less memory capacity than SOTA 
Achieve high linearity and over 90% MAC accuracy during MAC operations in TBA ([-288,+288])
Achieve high linearity and ultra-low power during Psum computation in CPA ([-1,152,+1,152])
Ternary-CIM is fabricated in TSMC 65 nm CMOS process
VDD = 1.0 V / Frequency = 250 MHz / Power = 1.59 mW / Capacity = 9.22 KB / Accuracy = 91.2 %
Achieve peak performance of 1,316 GOPS and 823 TOPS/W energy efficiency
<Performance Comparison Table>
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Activation and weight are all ternary precision
Achieve up to 11.43 times higher energy efficiency compared to SOTA
[11] X. Si et al., "A Twin-8T SRAM Computation-in-Memory Unit-Macro for Multibit CNN-Based AI Edge Processors," in IEEE J. Solid-State Circuits, vol. 55, no. 1, pp. 189-202, Jan. 2020.
[15] H. Valavi, P. J. Ramadge, E. Nestler and N. Verma, "A Mixed-Signal Binarized Convolutional-Neural-Network Accelerator Integrating Dense Weight Storage and Multiplication for Reduced Data Movement," in Proc. IEEE Symp. VLSI Circuits (VLSIC), 2018, pp. 141-142.
[19] S. Yin, Z. Jiang, J. -S. Seo and M. Seok, "XNOR-SRAM: In-Memory Computing SRAM Macro for Binary/Ternary Deep Neural Networks," IEEE J. Solid-State Circuits, vol. 55, no. 6, pp. 1733-1743, June 2020.
[13] Z. Jiang, S. Yin, J. -S. Seo and M. Seok, "C3SRAM: An In-Memory-Computing SRAM Macro Based on Robust Capacitive Coupling Computing Mechanism," in IEEE J. Solid-State Circuits, vol. 55, no. 7, pp. 1888-1897, July 2020.
[18] S. Jain, S. K. Gupta and A. Raghunathan, "TiM-DNN: Ternary In-Memory Accelerator for Deep Neural Networks," IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 28, no. 7, pp. 1567-1577, July 2020.
<Photograph of Chip Layout and Chip Specification>
<Simulation Results for Ternary-CIM>
< Multi-bit CIM and Binary CIM>
Multi-bit CIM
  Image classification accuracy 
  Energy efficiency 
Binary CIM
  Image classification accuracy 
  Energy efficiency 
 Ternary Neural Network (TNN): compromise 
<Ternary-CIM for Ternary Neural Network Acceleration>
Ternary-CIM
  3 Ternary Bitcell Banks (TBB)
  4 Ternary Bitcell Arrays (TBA)
  96×32 16T1C Ternary Bitcell in each TBA
  4 Charge-based Psum Adder (CPA)
Ternary-CIM enables efficient TNN operation, with pipelined TBA/TBB