## Slide 1
96.48% Peak-Efficiency Continuous-Current Step-Up Battery Charger (CC-SUBC) with Dual Energy-Harvesting Sources for Automotive Application
Hyo-Jin Park, Young-Jun Jeon, Young-Ju Oh, and Sung-Wan Hong
School of Electronics Engineering, Sogang University
Design Procedure
Result
Conclusion
CC-SUBC has the largest maximum output power among the step-up converters.
Among the converters, CC-SUBC is the sole converter having two input sources.
Among the step-up converters, only CC-SUBC has a continuous IO.
<Acknowledgement>
The EDA tools were supported by the IC Design Education Center (IDEC), South Korea.


Positive Feedback Loops
Adaptively increase bias current
Possible to improve slew-rate
Keep static power consumption small
Buck charger
- Continuous output current
- Inefficient use of harvesting cells


Boost charger
- Discontinuous output current
- Efficient use of harvesting cells
Continuous-Current Step-up battery charger (CC-SUBC)
Continuous output current
Efficient use of harvesting cells
Dual harvesting sources



- Operation of the CC-SUBC
- Duty determination and relationship between iL1 and iL2
Circuit Explanation
Circuit Architecture
2 input, 1 Flying capacitor, 2 inductors, and 6 switches
Reduce the power loss by making the minimum RON of switches
 Operation of the proposed charger with a single & dual input source
Peak efficiency was 96.48% (VBAT=10V, VTEG=3V and VPV=4.5V )
