## Slide 1
248 GHz Compact Mixer-Last Direct-Conversion Transmitter with I/Q and LO Feedthrough Calibration Capability
Seunghoon Lee, Junhyeong Kim, and Ho-Jin Song Electrical Engineering, POSTECH, Pohang, Korea
Abstract
- This paper presents a 248 GHz compact direct-conversion transmitter (TX) with IQ imbalance and LO feedthrough (LOFT) calibration capability, which can achieve a data rate of 20-Gb/s with 16-QAM. The measured image rejection ratio (IRR) and LOFT suppression are better than 25 and 28 dB, respectively, within the range of 242–252 GHz.
Introduction
- The sub-terahertz band above 200 GHz has attracted research interest due to its wide frequency bandwidth and compact hardware size [1].
- Extensive research has been conducted on developing TXs operating above fmax. There are generally three structures:
Transmitter Design
High output power
Not suitable for high-order constellation
Spectral broaderning
Multiplier-last TX
PA
RF
LO
IF
x N
High-performance
High power consumption
Large area
Cubix mixer-last TX
RF
LO
IF
Simple structure
High power consumption
Long LO chain
Mixer-last TX
LO
IF
x 2
x N/2
 In this work, a 248 GHz direct conversion transmitter with a push–push sub-harmonic double-balanced mixers has been developed, which is capable of IQ and LOFT calibration capability. It achieves a maximum data rate of 20-Gb/s with low power consumption and a compact size.
Fig. 1. 248 GHz CMOS transmitter architecture.
Fig. 2. Schematic of push push sub-harmonic double-balanced mixers.
70Ω, 90º@LO1/2
100Ω
50Ω, 19º
70Ω, 40º
70Ω, 90º@LO1/2
LO1/2 (1)
LO01/2 (2)
LO451/2 (3)
Fig. 3. Schematic of 0/45-degree generator.
Fig. 6. nth harmonic output power.
LO Multipliers (x8)
  Employs x4 and x2 to efficiently produce the eighth harmonic with low power and size.
  The simulated peak output power is -2.46 dBm at 136 GHz with a harmonic suppression greater than 24 dB and a power consumption of 31 mW.
M1 : 30/40nm
M2 : 114/40nm
I+
VG1
LO01/2 + (f0/2)
RF+
RF−
60Ω
M1
12.4 fF
VG1
LO01/2 − (f0/2)
I−
M2 M2
M1
M2 M2
60Ω
12.4 fF
Q+
VG1
60Ω
M1
12.4 fF
VG1
Q−
M2 M2
M1
M2 M2
60Ω
12.4 fF
LC series
harmonic mixer
LC series
harmonic mixer
LO451/2 + (f0/2)
LO451/2 − (f0/2)
130um
130um
f0
f0
f0
f0
IQ current combiner
LOFT calibration
C ↓ (VG 0.1−0.9 V)
Varactor VG ↑ (0.1-0.9 V)
Fig. 4. Simulated phase difference; Simulated gain.
Push-Push Sub-Harmonic Double-Balanced Mixers
  The conversion gain is improved by 3 dB through the reduction of the body voltage in quad-transistors and the addition of an LC series circuit.
  Reduces size by requiring LO frequency that is half of RF frequency.
Low-Loss 0/45º Generator with Phase Controllability
  employs a Wilkinson power divider and a transmission line terminated with capacitive loads for low loss and phase controllability, which can necessitate only a 2-stage LO buffer amplifiers, as opposed to a 3-stage configuration.
RF
x N
Fig. 5. Schematic of frequency multipliers.
Measurement
mixer
+balun
LO generation
2-stage
buffer
1.34 mm
0.64 mm
Signal Generator
(Keysight N5183B)
Signal Generator
(Keysight N5183B)
AWG
(Keysight M8195A)
I+
I-
Q+
Q-
TX module
LO1/16
External
sub-harmonic mixer
DSO
(Keysight DSOV254A)
RF
VDI D-band extension module (×12)
Fig. 7. A photograph of die chip.
Fig. 8. Measurement setup.
Fig. 9. Measurment setup photo.
Fig. 10. Measured LOFT, IRR.
Fig. 11. Output power, conversion gain
Fig. 12. Constellation measurement
Modulation | QPSK | 16 QAM | 32 QAM
Baud rate (Gbaud/s) | 9 | 5 | 2
EVM (dB) | -12.26 | -17.37 | -18.81
Chip/core size : 1.34  0.64 mm2, 0.4 mm2; consumped DC power : 96.3 mW.
LOFT and IRR after calibration were improved by approximately 20 dB at 245 GHz and maintained above 28 dB and 25 dB in the range of 242 GHz to 252 GHz.
The conversion gain and output P1dB of the DCT were 14.78 dB and -19.81 dBm, respectively.
The 3-dB bandwidth was 10 GHz from 243 GHz to 253 GHz including PCB, cable loss.
A peak data rate of 20 Gb/s was measured at 248 GHz using the 16-QAM.
 | [2] JSSC 2018 | [3] JSSC 2015 | [4] ISSCC 2017 | [5] IMS 2020 | [6] JSSC 2022 | This work
Technology | 130nm SiGe | 65nm CMOS | 40nm CMOS | 65nm CMOS | 65nm CMOS | 40nm CMOS
Frequency (GHz) | 240 | 240 | 300 | 288 | 256 | 248
TX architecture | Direct-conversion TX | Multiplier last | Cubic mixer last | Mixer last | Mixer last | Mixer last
Integrated TX circuit blocks | LO mult. (×8), LO amp., IQ gen., BB amp., IQ mixer, PA. | LO mult. (×2), ILFM, IQ gen., IQ mixer, PA, Frequency multiplier (×3), On-chip antenna. | LO mult. (×3), SSB mixer, Amplifiers, Square mixers. | LO mult. (×3), LO amp., IF amp., Sub-harmonic mixer. | LO mult. (x4), LO amp., PS, IF amp., sub-harmonic mixer. | LO mult. (×8), LO amp., IQ gen., IQ sub-harmonic mixer.
I/Q calibration | - | - | - | - | Yes | Yes
LOFT calibration | - | - | - | - | Yes | Yes
Conversion gain (dB) | 10.5 | - | -8** | 8** | - | -14.78
Data Rate (Gb/s) | 25 | 16 | 105 | 34 | 52 | 20
PDC (mW) | 375 | 220 | 1400 | 270 | 750 | 96.3
Area (mm2) | 1.25 | 2 | 5.2 | 1.9 | 4.17*** | 0.86
Reference [1] H.-J. Song et al., IEEE TTST, 2022. [2] M. H. Eissa et al., IEEE JSSC, 2018. [3] S. V. Thyagarajan et al., IEEE JSSC, 2015. [4] K. Takano et al., ISSCC, 2017. [5] I. Abdo et al., IMS, 2020.
[6] I. Abdo et al., IEEE JSSC, 2022.
Acknowlegement Chip fabrication was supported by the IC Design Education Center.
20 dB
20 dB