## Slide 1
Low Power Comparator Operation with Predictor
for Spiking Neural Network
Gyuwon Kam, Dahyeon Youn, Jiin Moon, Sooyoun Kim, Minkyu Song
Department of Semiconductor Science, Dongguk University
onegg99@dgu.ac.kr
Through integration & fire process, spike comes out and neuron with a large number of output spike are inferred as the answer.
This study implements a SNN system optimized for the MNIST dataset in hardware.
4. Simulation results
With the creation of a large amount of data, Von Neumann Archtecture has limitation in processing. As a result, neuromorphic computing technology of low-power and high-efficiency operations is required.
SNN (Spiking Neural Network) is a neuromorphic system based on biological neural network operations in the brain.
2. Main concept
Figure (a) shows a section that does not require a comparator operation, and figure (b) shows a neuron that does not require a comparator operation.
9 Pixel
6 Post
Full chip
Full Block diagram
 | VDD = 1.8V | Neuron
w/o Predictor | Current | 3.682uA
 | Power | 6.627uW
w/ Predictor | Current | 2.580uA
 | Power | 4.643uW
Case1. Large weight
29.94% ↓
 | VDD = 1.8V | Neuron
w/o Predictor | Current | 3.742uA
 | Power | 6.736uW
w/ Predictor | Current | 2.580uA
 | Power | 3.751uW
Case2. Small weight
44.31% ↓
This study proposes prediction block to reduce the neuron power consumption by predicting the output spike. In the SNN system, even when the difference between the membrane voltage and the threshold of the neuron is large, the comparator always operates and consumes unnecessary power. When the difference between the membrane voltage and the threshold voltage is 100 mV or less, the predictor generates a signal that operates the comparator. The prediction block reduces the neuron's power consumption during inference by more than 30%
SNN system with 9 input, 6 output nodes was implemented through a circuit, and the low-power operation of the neuron circuit was aimed.
The chip fabrication was supported by
the IC Design Education Center(IDEC), Korea.
1. Spiking Neural Network
Von Neumann Architecture
Pre-neuron
Synapse
Post-neuron
inference
<4>
<3>
<5>
.
.
.
weight
membrane voltage
(a)
Vth
Vmem
(b)
Vth
Vmem
Considering the power consumption of the comparator, this study propose a prediction circuit that sends an ENA signal that operates the comparator only when necessary.
3. Neuron circuit
The synapse current is flowed through the current mirror, and the membrane voltage is increased by the capacitor.
The ENA signal is turned on when exceeding Vpd(prediction voltage). The comparator operates when the ENA signal is turned on, and the spike comes out when Vmem(membrane voltage) is higher than the Vth(threshold voltage).
w/ Predictor
w/o Predictor
Vth
Vpd
ENA
POST
Bottleneck