## Slide 1
Background
The clock and data recovery (CDR) circuit is one of the most important building blocks for wireline serial communication receivers.
The CDR without reference signal was proposed for the interfaces that covers continuously changed data rates. The reference-less-type CDR has the advantage of reduced interference from external reference signals during CDR operation. So, the reference-less-type CDRs are widely used in many applications because of their simplicity, flexibility, and low cost.
Many studies on reference-less CDR, the increasement in power consumption due to the necessity of frequency loop and the power limit imposed by high-speed signals remains unresolved issues. Also, as the data rate is increased, the power dissipations of flip-flops and XOR gates, which are the major speed bottlenecks of the PD and FD, are also increased. The present research proposes a subsampling PD/CP (SSPD/CP) and FD (SSFD) to overcome the speed bottleneck and limit of power consumption.
Proposed Design & Results
Conclusion
This brief describes 0.7-pJ/b 12.5-Gb/s 1/5-rate reference-less subsampling CDR circuit.
The proposed frequency loop is configured in a monotonic manner, effectively addressing the shortcomings of SSPD/CP, such as a narrow capture range.
This design features a power consumption of 8.8mW and an energy efficiency of 0.7 pJ/bit. Jitter performance is 3.7psrms, 21pspp. JTOL is exhibited 0.52UIpp at 100MHz.
Reference
[1] K. Park et al., “A 4–20-Gb/s 1.87-pJ/b continuous-rate digital CDR circuit with unlimited frequency acquisition capability in 65-nm CMOS,” IEEE J. Solid-State Circuits, vol. 56, no. 5, pp. 1597–1607, May 2021.
[2] C. Yu, E. Sa, S. Jin, H. Park, J. Shin, and J. Burm, “A 6.5– 12.5-Gb/s half-rate single-loop all-digital referenceless CDR in 28-nm CMOS,” IEEE J. Solid-State Circuits, vol. 55, no. 10, pp. 2831–2841, Oct. 2020.
[3] S. Huang et al., “An 8.2-to-10.3Gb/s full-rate linear reference-less CDR without frequency detector in 0.18µm CMOS,” IEEE J. Solid-State Circuits, vol. 50, no. 9, pp. 2048–2060, Sep. 2015.
Acknowledgement
The chip fabrication was supported by the IC Design Education Center(IDEC), Korea.
A 0.7-pJ/b 12.5-Gb/s Reference-Less Subsampling Clock and Data Recovery Circuit
Yoonsang Lee, Jongchan An, Mingyun Kim, and Junyoung Song*
Dept. of Electronics Engineering, Incheon National University, Incheon, South Korea
Fig. 1. Block diagram of the proposed reference-less CDR.
Fig 2. Timing diagram of the SSPD/CP
Fig. 4. Measurements Results & Die micrography & Power break down
Fig. 3. Block diagram of the proposed SSFD and false-lock detector
characteristic curve and transient response.
TABLE I
PERFORMANCE COMPARISON TABLE