## Slide 1
A W-band Bidirectional Variable Gain Vector-Sum Phase Shifter Using a Directional Coupler
Sungwon Kwon and Byung-Wook Min
Department of Electrical and Electronic Engineering, Yonsei University, Seoul, Korea
Conclusion
Designed a passive, bidirectional VSPS.
Phase shifting through a 22.5 ° switchable directional rat-race coupler and transistor switches.
The variable gain states of all phase-shifted states are achieved independently using the X-ATTS.
All phase-shifted and variable gain states without calibration.
Proposed P-VSPS is suitable for large-scale phased-array systems with bi-directional characteristics, variable gain operation, calibration free, low phase/gain error, low insertion loss and zero power consumption.
Abstract
28-nm CMOS W-band Vector Sum Phase Shifter
Separated phase and gain control without any calibration
Using 22.5˚ switchable directional coupler and switches for phase control
Using X-type attenuators for variable gain control
Chip Size : 0.63 x 0.25 (0.16mm2)
Design Concept
Schematic
Measurement Results
Average insertion loss : 13.2±0.7 dB @ 94GHz
SPDT, DPDT based 360° 4-bit Phase Shifter
RMS phase error 2.4° at 0 dB gain control
RMS amplitude error 0.5 dB at 94 GHz
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Chip Microphotograph
Circuit Design
Switching the I and Q signals of a coupler through an absorptive SPDT
A X-ATT consists of equally sized cross-connected transistors.
Using coupled-line couplers for I/Q generation for compact chip size and wide bandwidth
Notes: 안녕하세요 연세대학교 전기전자공학과 소속 통합 4년차 권성원입니다.
본 포스터에 게재되어 있는 "Bidirectional Vector Sum Phase Shifter"에 대해 소개하도록하겠습니다.
먼저, 제안된 phase shifter는 28-nm CMOS공정기반의 W-band에서 동작하는 회로입니다.
VGA나 ATT없이, 신호감쇠를 최소화 해서 벡터 summing을 구현한 것이 본 phase shifter의 특징입니다.
또한 대칭으로 동작하는 SPDT, DPDT를 사용함으로서 RMS amplitude error와 gain variation을 최소화 할 수 있었습니다.
또한, tunable RRC를 통해 추가적인 비트를 구현하였고, 칩 수령 및 측정이 추후 예정되어 있습니다.
다음으로, 이 회로의 디자인 컨셉에 대해서 설명하겠습니다.
상단의 그림은 기존의 Vector sum phase shifter들의 일반적인 동작원리를 설명하는 block diagram입니다.
기존의 VSPS의 경우 coupler와 같은 회로를 통해 I, Q signal을 나눈뒤, 한쪽의 신호만을 전달하거나, I,Q신호의 gain을 조절해서 phase shifting을 구현합니다.
우측 S21 polar plot에 글려진 Vo1과 V’o2가 그 예시라고 할 수 있습니다.
이때, 그림에서 보실 수 있다시피, V’o2의 경우 Vo1보다 Voltage 벡터합이 더큽니다.
이때문에, 추가적인 gain attenuation을 거쳐야만, Vo1과 동일한 크기의 gain을 만들어 낼 수 있습니다.
결론을 말씀드리자면, 기존의 VSPS의 경우 phase shift에 따른 gain variation으로 인해, signal attenuation이 필요하다고 할 수 있습니다.
이 block diagram은 제안된 VSPS입니다.
제안된 phase shifter의 경우는 signal attenuation이 따로 없습니다.
그 대신, coupler의 input을 바꿈을 통해서 asymmetric power combiner의 전달되는 I신호와 Q신호를 스위칭합니다.
asymmetric power combiner는 의 I, Q 신호를 phase shifting을 위해 특정 비율로 신호를 combining합니다.
따라서 신호의 감쇠없이 vector summing을 구현할 수 있습니다.
다음은 세부 회로에 대한 설명을 드리겠습니다.
50옴 매칭을 유지하며 input signal의 방향을 바꾸기 위해Absorptive SPDT를 사용하고있습니다.
이렇게 설계된 회로는 신호가 isolate된 path에서도 50옴 매칭을 유지하고 있습니다.
개별 I, Q 신호의 +- 부호변환, 즉 180 위상변화를 위해서 dpdt balun을 사용하고있습니다.
마지막으로 asymmetric power combiner의 경우는 rat race coupler를 lumped component를 이용해서 구현했습니다.
이를 통해 size를 최소화하고 충분한 power combing ratio를 가져갈 수 있었습니다.
측정 결과를 보면, 평균 삽입 손실은 85GHz에서 13.1±0.5 dB로 측정되었습니다.
85 GHz에서 RMS 위상 오차는 4.1°, 80 GHz에서부터는 6.9° 미만으로 측정되었습니다. 또한, 85 GHz에서 RMS 진폭 오차는 0.3 dB, 80 GHz에서 92 GHz 사이에서는 0.5dB 미만으로 측정되었습니다.
이상으로 발표를 마치겠습니다. 감사합니다.