## Slide 1
13-15 GHz Passive Variable-Gain Switched Phase Shifter with X-Attenuator using 28-nm Bulk CMOS
Min-Seok Baek, Jae-Hyeok Song and Choul-Young Kim
SCDL, Department of Electronics Engineering, Chungnam National University, Korea
Driven by high-speed data demands, the Ku-band (13.75–14.6 GHz uplink) has become a key spectrum for SATCOM.
In SATCOM phased arrays, phase shifters enable precise beam steering by dynamically controlling signal direction, allowing flexible link optimization in mobile or multi-beam scenarios.
In this work, a Ku-band variable-gain phase shifter is implemented using an X-attenuator structure that enables 180° phase control and attenuation tuning, optimized for compact beam steering systems.
Frequency: 13-15 GHz
Topology: Passive Variable-Gain Switched Phase Shifter
Applied Technique:
    X-attenuator integrates a phase inverter, enabling a continuous 180° phase control range.
    Gain tuning is achieved through a voltage-controlled passive attenuation path with high linearity.
    A passive 5-bit switched-type phase shifter provides discrete phase control with no power consumption.
    The 90° phase bit adopts a hybrid high-pass/low-pass filter design for wideband phase flatness.
    Transistor sizes are optimized to balance insertion loss and phase slope sensitivity.
    Top-layer metal (M9) is utilized in inductors and transmission lines to minimize parasitic loss.
II. Circuit Design
I. Introduction
III. Simulation Result
Simulation Result:
    Frequency: 13-15 GHz
    Phase Resolution: 0~360˚ (LSB=5.625˚)
    Attenuation Range: 25 dB
Ref. | This Work (Sim.) | [1] IMS’24 | [2] ICMMT’19 | [3] ACCESS’22
Process | 28-nm CMOS | 0.13-um SiGe | 0.13-um CMOS | 65-nm CMOS
Technique | X-atten. with STPS | STPS+ RTPS | High Pass / Low Pass | Low Pass LC
Freq. (GHz) | 13 - 15 | 14 - 15 | 8.5 – 10.5 | 5-11
RL (dB) | > 9 | > 8.4 | > 13 | > 10
IL (dB) | 9.08 – 10.8 | 4.3 - 8.1 | 14 | < 41
RMS PE (˚) | 0.7 – 1.75 | < 12 | 4 | < 5.2
RMS GE (dB) | 0.17 - 0.27 | < 1.1 | 0.4 | -
Power (mW) | 0 | 0 | 0 | 0
Core Area (mm2) | 0.3 | 0.17 | 3.52 | 2.46
The proposed variable-gain PS was designed using a 28-nm Bulk CMOS process. The PS demonstrates superior performance compared to other literature in the field.
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Fig. 2. Full Schematic of Variable-Gain Phase Shifter
Fig. 3. Phase/gain response with voltage variation in the X-atten.
Fig. 1. Block Diagram of Variable-Gain Phase Shifter
IV. Conclusion
Fig. 5. S-parameter Simulated results
[1] S. Kim, K. W. Choi, B. Yoon, J. Kim and I. Ju, "Compact, Low Loss 4-Bit Ku-Band Hybrid Passive Phase Shifter Realized in 0.13-μm SiGe HBT BiCMOS for LEO SATCOM," 2024 IEEE/MTT-S International Microwave Symposium - IMS 2024, Washington, DC, USA, 2024, pp. 760-763.
[2] S. Wu and D. Pang, "A 6-bit CMOS Passive Phase Shifter for X-Band Phased Arrays," 2019 International Conference on Microwave and Millimeter Wave Technology (ICMMT), Guangzhou, China, 2019.
[3] J. -M. Song and J. -D. Park, "A 5–11 GHz 8-bit Precision Passive True-Time Delay in 65-nm CMOS Technology," in IEEE Access, vol. 10, pp. 18456-18462, 2022.
Fig. 4. Full Layout of the Variable-Gain Phase Shifter