## Slide 1
Design and Analysis of Reference-less Dynamic Comparator for PAM-4 Receiver
Tae-Gu Kang, and Jin-Ku Kang
Department of Electrical and Computer Eng., Inha University, Incheon, Korea
Introduction
This paper analyzes how the effective least significant bit (LSB) threshold voltage of conventional dynamic comparators varies with respect to the variation of the common-mode level of input voltages. And this paper proposes a reference-less dynamic comparator to overcome the problem. The proposed dynamic comparator has been designed and simulated at post layout level in a 45nm CMOS with 1.1V supply voltage.
Result and Discussion
The block diagram of the proposed structure is shown in Fig. 1.
where , , and represent linear
preamplifier and are non-linear summers.
Threshold voltage can be expressed as follows
.
VCP, VCN, and VBB are independent of VIN,CM due to the
common-mode rejection capability of the differential amplifiers,
which results in less variability in .
Fig.2 shows the on variation for Strong-ARM
latch, double-tail, and the proposed comparator-based
decision circuitries, Respectively.
Strong-ARM and double-tail structures have 406.9 mV and
527.7 mV of variations of respectively, over = 500 mV through = 1.1 V.
In contrast, the proposed structure has 79.7 mV of variation.
Fig. 3 shows the BER test results. The Bathtub widths for BER = 10-4.5 are 220 mV, 100 mV, 40mV, and 420 mV for Strong-ARM latch, double-tail, timebased, and proposed comparator-based decision circuitries, respectively. The proposed structure has better BER than other structures due to less variability of .
Conclusion
This paper presents a dynamic comparator with less variability in the effective LSB threshold voltage than the conventional dynamic comparators due to the common-mode-rejection capability.
Acknowledgement
This work was supported by Inha University. CAD tools and chip fabrication were provided by IDEC.
Fig. 1. schematic of proposed reference-less dynamic comparator
Fig. 2. Effective LSB threshold voltage on
VIN,CM variation
Fig. 3. BER of LSB on VIN,CM variation