## Slide 1
Results
This study focuses on the design and implementation of a high-speed Serializer/Deserializer (SerDes) circuit.
In TX mode, a 32-bit Parallel Data Signal with a Data Rate of 500MHz is received from the ATE and converted into a 1-bit Data Signal with a 16GHz Data Rate using a two-stage 4-to-1 Serializer followed by a 2-to-1 Serializer. The fully Serialized Signal is then delivered to the Output Driver, sampled through a True Single-Phase Clock Flip-Flop, and output via an Inverter Chain.
In RX mode, a 1-bit Signal with a Data Rate of 16GHz is converted to a Differential Signal through a Single-to-Differential Buffer (SDB) and equalized in the Continuous Time Linear Equalizer (CTLE). The Signal is then Deserialized back into a 32-bit Parallel Data Signal with a Data Rate of 500MHz.
The Serializer design employs True Single-Phase Clock (TSPC) DFFs to perform Data Timing Align. Each stage uses Transmission Gates and an OR Gate Equivalent Circuit with a Ring Counter Clock for Serialization. To improve area efficiency and reduce Propagation Delay, the OR Gate is replaced with NAND Gates and Inverters.
Department of Electrical and Electronic Engineering, College of Engineering, Yonsei University, Republic of Korea
Department of Electronics Engineering, College of Engineering, Incheon National University, Republic of Korea
Keywords – SERDES, CTLE, CDN, SDB
The Serializer, as shown in Fig. 1, is designed with a 4-to-1 Serializer, a 2-to-1 Serializer, and a Clock Distribution Network for its operation. Each Serializer block is based on TSPC DFF architecture. At the Serialization Output Node, a recursive configuration of Transmission Gates is employed to ensure robust and intuitive Data Serialization.
As mentioned in previous results, this design achieves significant cost advantages in terms of chip area and power consumption compared to similar processes. It also demonstrates a certain level of efficiency when compared to more advanced processes. Therefore, this design can be robustly applied to any SERDES system utilizing a 65nm process. Furthermore, it is designed to be directly applicable to higher data rates beyond the one proposed in this paper.
A. Transmitter with Serializer & Output Driver
Conclusion
Introduction
To generate the Clock required for the operation of the Serializer in Fig. 1, a Frequency Divider and a Set Generator, as shown in Fig. 2, are necessary to initiate the first operation of the Ring Counter. The operation of the Set Generator is described in the accompanying Timing Diagram.
The Data Signal, after completing Serialization through the Serializer, is driven via an Output Driver, as shown in the right-hand schematic of Fig. 3. Since the Data Rate of the Sampling Clock must match the Data Rate of the Output Data, the Serializer requires Clock Doubling. To achieve this, a Frequency Doubler, as depicted on the left side of Fig. 3, was designed to generate the necessary Clock.
[1] J. Jang, H. Lim and T. W. Kim, "A CMOS Complementary Common Gate Capacitive Cross-Coupled Frequency Doubler," in IEEE Transactions on Circuits and Systems II: Express Briefs, vol. 69, no. 9, pp. 3694-3698, Sept. 2022
[2] S. Vehring, Y. Ding, P. Scholz and F. Gerfers, "A 3.1-dBm E-Band Truly Balanced Frequency Quadrupler in 22-nm FDSOI CMOS," in IEEE Microwave and Wireless Components Letters, vol. 30, no. 12, pp. 1165-1168, Dec. 2020
[3] Y. Ye, B. Yu, A. Tang, B. Drouin and Q. J. Gu, "A High Efficiency E-Band CMOS Frequency Doubler With a Compensated Transformer-Based Balun for Matching Enhancement," in IEEE Microwave and Wireless Components Letters, vol. 26, no. 1, pp. 40-42, Jan. 2016
Fig 1. Serializer & CDN for Serializer Schematic
Fig 2. Frequency Divider & Set Generator in CDN
with Set Generator Timing Diagram
Fig 3. Output Driver With Frequency Doubler
B. Receiver with SDB w/ CTLE & Deserializer
Fig 4. Single to Differential Buffer & Continuous Time Linear Equalizer
Fig 5. Deserializer & CDN for Deserializer Schematic
The Receiver consists of a Continuous Time Linear Equalizer (CTLE) and a Single-to-Differential Buffer (SDB) to provide input to the CTLE. The SDB adopts a CS+CG structure, enabling a 180-degree phase shift of the Single-Ended Data Signal. A Differential CS Amplifier is subsequently used to attenuate Noise and compensate for Gain. The output Signal is then fed into the CTLE, where the Nyquist Frequency corresponding to the Target Data Rate is boosted to perform Equalization. In this study, the design compensates for approximately 11dB of Gain at the Nyquist Frequency of 8GHz for a 16Gbps Data Rate. Additionally, the Zero is designed at -10dB without fully suppressing the DC component.
Finally, the Equalized Signal is provided as input to the Deserializer. Deserialization is performed using a DET-based 1-to-2 Deserializer, as shown in Fig. 5. The required Clock for this process is generated by the Clock Distribution Network (CDN).
 | This Work | 2010' JSSC [1] | 2014' JSSC [2] | 2020' JSSC [3]
Data Rate | 16Gbps | Dual Lane 40Gbps | 1.25G - 28.5Gbps | 112Gbps
Modulation | NRZ | DQPSK | NRZ | PAM4
Chip Size | 2 X 3 mm2 | 4 X 4 mm2 | 1.8 X 1.85 mm2 | 0.75 X 0.375 mm2
Power consumption | 670mW | 3W | 560mW at 28Gbps | 448mW
Process | 65nm CMOS | 65nm CMOS | 28nm CMOS | 10nm FinFET
As shown in Table 1, this design demonstrates efficient utilization of power consumption, chip area, and intuitive modulation, effectively meeting the cost requirements of the SERDES.
Table 1. SERDES Specification Comparison
16Gbps High Speed Interface Module with SERDES & CTLE
Lee Dong Gun, Tae Soo Ahn, Jong Chan An, Tae Wook Kim, Jun Young Song
Abstract
Acknowledgement The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.