## Slide 1
Introduction
Proposed Scheme: Slope-Based Sampling for Long-Tail ISI Robustness
A cross-self-referenced architecture with a hysteresis-controlled sampler is adopted to improve ISI robustness.
Measurement
The proposed receiver achieves robust horizontal margin across various channel conditions with severe long-tail ISI (up to 0.545).
Measured BER bathtub curves demonstrate stable operation under high channel loss.
Conclusions
The proposed slope-based sampling receiver achieves robust operation under severe long-tail ISI conditions.
By employing a cross-self-referenced hysteresis-controlled sampler, it enhances the vertical margin without requiring complex equalization.
A 0.092-pJ/bit and 7.7-fJ/bit/dB Cross-Self-Referenced Slope-Sampling Receiver with Long-Tail ISI Robustness for Next-Generation Low-Power Memory Interfaces
Ki-Soo Lee*, Chanheum Han*, and Joo-Hyung Chae (*Equally-contibuted Authors)
Electronics and Communications Engineering, Kwangwoon University
Acknowledgement The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Severe channel loss in high-speed memory interfaces causes long-tail ISI and degrades sampling margin.
Voltage-based sampling suffers from low common-mode operation and ISI accumulation.
This work employs slope-based sampling to enhance vertical margin and robustness to ISI without any equalization.
Implementation
In voltage-based sampling, post-cursor ISI components are directly accumulated, leading to degraded signal integrity as the number of post-cursors increases.
In contrast, slope-based sampling utilizes the differences between adjacent coefficients, enabling partial cancellation of post-cursor ISI components.
As shown in the analysis, voltage-based sampling exhibits increasing mean and variation of accumulated ISI, whereas slope-based sampling maintains lower and more stable values.