## Slide 1
Simulation Results
A 0.58 Ops/Trans Analog Compute-in-Memory Macro With Input Operand Generator Supporting Wide Boolean Operations for Enhanced Versatility
Eun-Bi Koh, Jeong-Eun Ko, and Joo-Hyung Chae
Department of Electronics and Communications Engineering, Kwangwoon University
Introduction
Acknowledgement The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
The proposed architecture is based on three key ideas:
① 10T1C SRAM Bitcell with Capacitive Coupling
→ Enables charge-domain MAC with high linearity and no
threshold voltage loss.
② Input Operand Generator
→ Generates dual inputs (IN_L, IN_R) to support six Boolean
operations.
→ Achieves high versatility with minimal peripheral overhead.
③ Quaternary-Search 6-bit ADC
→ Performs 2-bit/cycle conversion to reduce latency.
→ Shares one ADC across three columns to minimize area
overhead.
Compute-in-memory (CIM) reduces data movement and improves energy efficiency for data-intensive applications.
However, most prior CIM macros are optimized for multiply-and-accumulate (MAC) operations, limiting their applicability.
To support a wider range of tasks, recent applications require both MAC and Boolean operations.
This work proposes an analog CIM (ACIM) macro that supports both MAC and multiple Boolean operations, while reusing the memory array structure in the analog-to-digital converter (ADC) to improve area–latency efficiency.
① 10T1C SRAM Bitcell
② Input Operand Generator
③ Quaternary-Search ADC
Overall Architecture
Proposed Architecture and Key Ideas
The proposed ACIM macro supports both MAC and six Boolean logic operations.
The row-shared IOG and quaternary-search ADC reduce peripheral overhead and improve area–latency efficiency.
Compared with recent CIM designs, this work achieves competitive energy efficiency of 33.8 TOPS/W.
Conclusion
VMAC exhibits highly linear behavior across MAC values under FF/TT/SS corners.
ADC outputs accurately match MAC values, validating correct conversion.
33.8 TOPS/W (energy efficiency)
0.58 Ops/Trans (Boolean operations per transistor)
89.81% inference accuracy for AND-based MAC operations (ResNet-18, CIFAR-10)