## Slide 1
그림
그림
그림
그림
그림
그림
Conclusion: This work presents a single-channel speculative loop-unrolled SAR ADC in 28-nm CMOS that reduces the CDAC-settling bottleneck through speculative switching and improves accuracy with comparator offset calibration. Simulation results show 5.21 bits ENOB at low frequency and 4.68 bits ENOB at Nyquist, validating the proposed high-speed single-channel SAR ADC.
그림
그림
Calibration logic without extending the critical timing path
Calibration for both CDAC1 and CDAC2 branches
Modified double-tail comparator for reduced kickback noise
Motivation
Top architecture employs speculative switching to reduce CDAC settling time.
Top Architecture
CDAC Switching Operation
Acknowledgement: The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
(a) Waveform of speculative CDAC switching.
(b) Binary Search Operation with Speculative CDAC Switching at 4-bit.
(a) Conceptual CDAC settling behavior.
(b) Timing comparison with speculative CDAC preparation.
TOP Design
Simulation Results
Maintains ENOB at both (a) low-frequency and (b) Nyquist inputs
Calibration enables improved SNDR/ENOB consistency
ENOB at Low Frequency: 5.21 bits
ENOB at Nyquist Frequency: 4.68 bits
RDAC Array
A 6-bit RDAC array generates programmable calibration voltages.
Its outputs are applied to each comparator branch for offset trimming through I2C control.
This supports accurate comparator offset calibration.
Conventional Loop-unrolled SAR ADC
Abstract: This chip implements a single-channel speculative loop-unrolled SAR ADC in 28-nm CMOS for high-speed conversion without time interleaving. Comparator offset calibration compensates for mismatch among parallel comparators, improving conversion accuracy and mitigating SNDR degradation.
Comparator Offset Calibration for 6-bit Single-Channel Speculative Loop-Unrolled SAR ADC in 28-nm CMOS
Dong-Un Jin1 and Min-Seong Chooa
1School of Electrical Engineering, Hanyang University, Ansan, South Korea
aSchool of Electrical and Electronic Engineering, Yonsei University, Seoul, Soutth Korea
(a)
(b)
Timing Advantage
Comparator with Offset Calibration
(a)
(b)
(a)
(b)
Conventional SAR: speed limited by sequential loop delay.
Comparator/logic delay → bottleneck.
Loop-unrolled SAR: removes loop delay, boosts speed but CDAC Settling time remains.