## Slide 1
A Wideband D-Band Variable Gain Amplifier for Phased-Array Systems
Songmi Je, Dongkyo Kim
Dong-A University, Dept. of Electronic Engineering
A D-band VGA using a triple-transformer input network was implemented in 28-nm CMOS.
The measured results demonstrate 7.7 dB peak gain, 15.6 dB gain control range, and 118.7-136.5 GHz bandwidth, verifying its suitability for mm-wave phased-array front-end applications.
The proposed VGA uses a triple-transformer input network for compact D-band implementation.
A 4-stage active cross-coupling neutralization (ACCN) structure is adopted, with the second stage serving as the gain control stage.
Compared with the conventional input network, the proposed structure eliminates DC-blocking capacitors.
D-band phased-array systems require front-end circuits that can compensate for large path loss and gain variation across array elements.
A variable gain amplifier (VGA) is an essential block for equalizing gain among channels and improving beamforming accuracy.
Design
Introduction
Measurement Results
Conclusion
Peak gain : 7.7 dB @ 127 GHz
Gain control range : 15.6 dB
3-dB BW : 118.7 – 136.5 GHz
DC power consumption : 30-37 mW
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.