## Slide 1
RS-CIM: Area-efficient Compute-in-Memory with
R-DAC & SAR Hybrid ADC
Kyuhyun Lee, Jitae Bae, Jinyeong Choi, Soo Youn Kim, and Minkyu Song
Dept. of System Semiconductor, Dongguk University, Seoul, Korea
E-mail : qowlxo102@student.dongguk.edu
Introduction
This paper proposes a high-area efficiency analog compute-in-memory(CIM) structure consisting of a 7T SRAM-based digital-to-time converter with clock multiplication and a hybrid ADC structure of a resistor-DAC and SAR ADC. Compared to conventional SAR ADCs and flash ADCs, the number of capacitors and comparators was reduced by 87.5% and 93.3%, respectively. As a result, we achieved 45.96 TOPS/W (247.7 TOPS/W*) and 0.46 TOPS/mm2 (6.498 TOPS/mm2*) in a 65nm CMOS process.(*scaling down to 28nm)
Motivation
Proposed R-DAC& SAR hybrid ADC based Compute-In-Memory (RS-CIM) Architecture
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Chip layout and Summary
Results and Discussion
 | DAC & ADC |  |  | 
 | Capacitor-DAC | SAR ADC | Current Steering-DAC | Flash ADC
Pros | low power  |  | high speed  | 
Cons | large area  |  | high power  | 
Compute-in-Memory(CIM) overcoming the memory bottleneck by integrating computation directly into memory
Previous A-CIM’s problems ① DAC&ADC’s CAP & comparator: Cell Density↓ ② using MUX: Column Parallelism↓
(a) CIM Paradigm
(c) Conventional A-CIM Limitations
 | Digital CIM (D-CIM) | Analog CIM (A-CIM)
Pros | - PVT immune  - high precision  | - high parallelism  - high energy efficiency  - low latency 
Cons | - low parallelism  - low energy efficiency  - bulky multiplier/adder  | - PVT variation  - DAC/ADC overhead 
(b) D-CIM vs A-CIM: Trade-offs
D-CIM vs A-CIM
 A-CIM: suitable for energy-efficient computing
 Optimized data converting units are required in an A-CIM.
① Proposed 7TC
② 8T compact SRAM cell
Features
[7T SRAM based digital-to-time converter(DTC) (7TC)]: linearity ↑ & Area ↓ - Capacitor-free design → smaller area than conventional DACs - Time-pulse input w/ Multiplying-DLL → high MAC linearity (R² = 0.9996)
[8T SRAM cell]: compact layout (1.8um×0.8um @ 65nm) - Row pitch matched to 7TC - Column pitch aligned with RS-ADC
System Flow input time pulses by 7TC → read-bit-line discharge → quantization by RS-ADC
- fully column parallel  computing density ↑; Requires just two unit capacitors, two TGSW, a 2N-2 bit DAC, and a single dynamic comparator
③ Proposed RS-ADC
*Based on 4-bit ADC
For N(4)-bit conversion | SAR ADC | Flash ADC | RS-ADC
# of Comp. | 1 | 2N-1 (15) | 1
# of CAP | 2N (16) | - | 2
# of RES | - | 2N-1 (15) | 2N-2 (4)
Latency (CLK) | N (4) | 2 | 2(N-1) (6)
(a) Comparison w/ SAR ADC & Flash ADC
RS-ADC significantly reduces # of capacitor (87.5%↓) and # of comparator (93.3%↓) compared to conventional ADCs, enabling area-efficient design.
RS-ADC analysis
(b) ADC comparison spec. table
 | JSSC 2024 | ISSCC 2023 | JSSC 2021 | JSSC 2023 | This work
Process | 28nm | 12nm | 28nm | 65nm | 65nm
Input/ Weight/ Output bit | 4,8/8 /N.A. | 8/8/8 | 4,8/4,8 /12,20 | 1~16/ 4,8,12,16/13,27 | 4/4/8
ADC bit | 4 | 8 | 5 | 4 | 4
ADC type | Flash | SAR & R-DAC | SAR | Integrating & SAR | SAR & R-DAC
Column Parallelism | 100% | 50% | 100% | 25% | 100%
Array size | 16kb | 128kb | 64kb | 12kB | 16kb
TOPS/W (scale to 28nm[5]) | 12.2~40.1 | 70.58~86.27(24.33~29.74) | 47.8~68.4* | 611.91** (2447.64) | 45.96 (247.7)
TOPS/mm2 (scale to 28nm[5]) | 0.84~2.86 | N.A. | 0.00038*★ | 0.83** (4.15) | 0.46 (6.498)
(a) Chip microphotograph and layout
*when input/weight/output bit is 4/4/12.
**when input/weight bit is 4/4.
★reverse calculation from GOPS & macro size.