## Slide 1
High-Integration Neuron Circuits
with Current-Scaling Integrators
Jiin Moon, Jaesang Han, Soo Youn Kim, and Minkyu Song
Dept. of System Semiconductor, Dongguk University, Seoul, Korea
E-mail : hjs4578@dgu.ac.kr
Introduction
This work proposes a current-scaling integrator (CSI) to enable high-density and low-power spiking neural network systems. CSI architecture performs proportional scaling of the synaptic input current, thereby reducing the required membrane capacitance by a factor of 1/n while preserving the membrane voltage for accurate spike timing. The proposed neuron achieves a 28% area reduction and an energy efficiency of 0.08 pJ/spike, representing a 61% energy reduction compared to the conventional capacitive transimpedance amplifier (C-TIA) implementation.
Proposed Neuron Circuit and SNN System
Simulation Results
Chip layout and Summary
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Process Tech. | Samsung 28nm CMOS
Classifier | Spiking Neural Network
Power Domain | 1.8V(Analog) / 1V (Digital)
Inference Dataset | MNIST
# Neurons | 35
Quantization Level of Weight | 9
Chip Size | 3.6 mm x 3.6 mm (Core : 1.98 mm x 1.65 mm)
Neuron Area | 2883 um2
Spike Pulse Width | 100 ns
System CLK Frequency | 10 MHz
Power Consumption | 32.4 μW/neuron
Accuracy | 94.82%* 91%**
Power Consumption & Area
A Super-Source Follower (SSF) is employed at the synaptic summing node to provide low input impedance.
The CSI scales down the summed synaptic current by a factor of 1/n.
Scaling mechanism reduces the required membrane capacitance (Cmem)
To minimize static power consumption, the proposed neuron operates without an OP-AMP, which is primary source of power overhead in conventional designs.
→ Enabling a high-density and low-power SNN implementation.
In this work, the proposed neuron was designed with a scaling factor of n = 2, providing the flexibility to enable or disable the current-scaling mechanism.
The observed linearity is consistent with the conventional C-TIA architecture, with an average error rate maintained within a comparable range. (approx. 4~5%)
(b) Block diagram of the proposed SNN architecture with CSI circuit
(a) CMOS circuit diagrams of the conventional C-TIA neuron
Chart: Current Linearity Simulation
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7
Neuron w/C-TIA | 0.10395 | 0.20754 | 0.3113 | 0.41523 | 0.51931 | 0.62355 | 0.72794
Neuron w/CSI | 0.10305 | 0.20953 | 0.31524 | 0.41963 | 0.52178 | 0.62132 | 0.71907
Neuron w /CSI (Scaling Mode) | 0.10379 | 0.20948 | 0.31509 | 0.42035 | 0.52488 | 0.62825 | 0.72997
Neuron w/C-TIA |  | 
Ideal Current [uA] | Error [uA] | Error Rate (%)
0.1 | 0.004 | 3.95
0.2 | 0.008 | 3.77
0.3 | 0.011 | 3.77
0.4 | 0.015 | 3.81
0.5 | 0.019 | 3.86
0.6 | 0.024 | 3.92
0.7 | 0.028 | 3.99
Neuron w/CSI (n = 2) |  | 
Ideal Current [uA] | Error [uA] | Error Rate (%)
0.1 | 0.004 | 3.79
0.2 | 0.009 | 4.74
0.3 | 0.015 | 5.03
0.4 | 0.020 | 5.09
0.5 | 0.025 | 4.98
0.6 | 0.028 | 4.71
0.7 | 0.030 | 4.28
(c) Simulated current linearity of the conventional C-TIA and the proposed CSI neuron (n=2)
(d) Inference results of the MNIST digit'7'
(e) Monte Carlo simulation of VRST and accuracy
System-level verification shows accurate MNIST inference (d) with Monte Carlo simulations (e), confirming 94.74% average accuracy under process variations.
(f) Area and energy consumption of different neuron circuit configurations
Power Consumption : Compared to the high-performance C-TIA (approx. 32 uW), the CSI configuration effectively reduces power consumption to around 17uW (with a 61% reduction in energy per inference).
Area Efficiency : The basic LIF and C-TIA configurations occupy approximately 3,000 um2 and 3,700 um2, respectively. In comparison, the proposed structure reduces the area to 2,883 um2 (a 28% reduction relative to C-TIA).
* Simulated (MATLAB)
** Measured
The proposed CSI-based SNN system was successfully integrated into a Samsung 28nm process with a core area of 1,985 um x 1,652 um.
Measurement results confirm that the fabricated chip achieves a 91% accuracy for the MNIST dataset while maintaining superior energy efficiency through its current scaling mechanism.