## Slide 1
Two-step ADC with Self-Successive Doubling
Algorithm for High-Speed CIS
Kyungmin Lee, Dongkyeong Lee, Wonyong Choi, Soo Youn Kim, and Minkyu Song
Dept. of System Semiconductor, Dongguk University, Seoul, Korea
E-mail : dlehdrud22@dgu.ac.kr
Introduction
This work proposed a hybrid circuit that enables simultaneous CDS operation and ADC by introducing a self-successive doubling algorithm. The SSD circuit converts the upper bits, and the SAR ADC converts the lower bits, significantly reducing the area required for C-DAC. The SSD shares a single amplifier for both CDS and ADC, eliminating extra amplifiers and power consumption.
Technology. | TSMC 180nm
Supply Voltage (V) (Analog / Digital) | 2.8 / 1.8
Resolution (V x H) | 124 x 148
A/D resolution | 12
Power consumption (mW)* | 7.54
Frame rate (fps) | 1161
1 row conv. time (μs) | 5.82
FoM [fJ/conv-step]** | 86.39
* Pixel amplifier + ADC power consumption
** FoM = (Power) / (# of pixel x Frame rate x 2ADC resolution)
Proposed Readout Circuit & Detailed Operation
<Measurement Environment>
<Measurement Result>
Measurement Result
Chip layout and Summary
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
The SAR ADC operates as a two-step ADC to reduce the required C-DAC area.
A residue amplifier is still needed for signal amplification.
The proposed circuit applies the SSD algorithm, enabling ADC conversion, correlated double sampling(CDS), and residue amplification to be performed simultaneously.
This approach effectively reduces both power consumption and chip area.
With VRST= 1V, VSIG = 509mV and VREF = 300mV, ΔV = 209mV and Vpp = 700mV
When Φset is enabled, charges are stored in the capacitor array using VREF and VSIG
During the SSD phase, capacitors switch between VREF and VIP, adjusting VIP based on the comparator output.
After six cycles, this process produces a binary code (e.g., 0100112) and the residue is amplified 64x for fine conversion
A and B represent the 2-bit binary code for the coarse part and fine part, respectively, whereas C represents the residue that is smaller than VFine.
At V0, since ‘A’ = 102, the coefficient for VCoarse at V1 is 1002 and V2 is 0002. B is 012, the coefficient of VFine becomes 01002.
Vn compares whether the amplified Vpp−ΔPD is higher than or lower than VRST.
 This demonstrates that the SSD algorithm can simultaneously perform CDS.
A typical analog CDS circuit is composed of switches, capacitors and a single amplifier, and the SSD circuit follows a similar structure.
Since the SSD circuit has a 6-bit ADC performance, the total capacitance of capacitor array is 26Cu , where Cu represents the capacitance of the unit capacitor.
Simple example of SSD operation