## Slide 1
A High-Efficiency Low-Power 6MS/s SAR ADC with Double Rail-to-Rail Operation
Jeetaeck Seo1 , JongHyeon Seo2 , Dong-Hyun Shin3 , Chunghee Jang4 , Jaesoub Han5 , Jeonghun Lee6 , Tae-hyun Kim7
and Kwang-Hyun Baek*
1Department of Intelligent Semiconductor Engineering, Chung-Ang University, Seoul, Korea
Abstract
A 0.007mm2 0.6V 6MS/s 10-bit SAR ADC with a double rail-to-rail input range, designed for extended application use, including compute-in-memory (CIM) systems. The proposed ADC achieves area efficiency by requiring only two additional series connected capacitors and a differential-difference comparator for double rail-to-rail operation. Furthermore, the set-and-down operation reduces the input referred noise of the comparator , achieving over ten times lower noise than complementary switching. To improve accuracy, a hybrid capacitor DAC, combining metal-insulator-metal(MIM) and metal-oxide-metal(MOM) capacitors is employed to minimize gain error
Introduction
Since ADCs contributed significantly to both power consumption and area in computer in memory (CIM) application, optimizing their efficiency is crucial. So, this proposal introduces a low power double rail-to-rail SAR ADC to expand applicability of low-power SAR ADCs in compute-in-memory (CIM) using only a single CDAC per side and reducing area requirements while maintaining performance
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
This paper was supported by Korea Planning & Evaluation Institute of Industrial Technology(KEIT)(2410000542, RS-2024-00403483) funded by the Ministry of Trade, Industry & Energy (MOTIE, Korea)
This paper was supported by Korea Planning & Evaluation Institute of Industrial Technology(KEIT)(RS-2025-02413438) funded by the Ministry of Trade, Industry & Energy (MOTIE, Korea)
Conclusions
This work presents a low-power double rail-to-rail SAR ADC that extends the input range for supply-scaled applications such as CIM. Area efficiency is achieved using only a series-connected capacitor and a DDC, while set-and-down switching improves comparator noise performance . A hybrid CDAC combining customized MOM and MIM capacitors minimizes gain error, making the ADC suitable for compact and wide-input-range CIM systems.
Fig. 5. (a) Measured static and dynamic performance
(b) Performance Comparison
(a)
(b)
1. Chip Implementation & Measurement Setup
Fabricated in 28 nm LPP process
Chip area: 4 mm × 4 mm (Mixed)
Core area: 0.007 mm2
Test board with power supply, Low Distortion Function Generator, Function Generator, Logic Analyzer
2. Measured Results & Comparison
DNL : +0.14/-0.09LSB , INL : +0.49/-0.46LSB
SNR : 53.90 dB , SNDR : 52.12 dB , SFDR : 60.39 dB (@ 100KHz Input Signal)
Fig. 4. (a) The layout of the proposed circuit
(b) Measurement setup for the proposed chip test.
Measurement Result
Proposed Double Rail-to-Rail SAR ADC
Proposed Architecture
The proposed SAR ADC achieves double rail-to-rail input range using FC-DACs, a Differential Difference Comparator, double-boost S/H switches, and SAR logic
The FC-DAC enables wide input conversion with reduced noise impact, while set-and-down switching improves comparator noise performance by lowering the input common-mode voltage
3. Proposed CDAC Architecture
Top-plate parasitic capacitance in the CDAC reduces the effective DAC step causing ADC gain error
The proposed hybrid CDAC uses customized MOM capacitors for the binary-weighted DAC and MIM capacitors for the floating capacitors
This structure minimizes parasitic-induced gain error, limiting input-range reduction to about 10% and achieving a 1.55 input range
Fig. 1. Proposed double rail-to-rail SAR ADC architecture
2. Set & Down Switching For Gain Enhancement
Double rail-to-rail operation increases the input range, but high input common-mode voltage degrades comparator gain and noise performance
Set-and-down switching lowers the common-mode during conversion, improving decision accuracy and enabling reliable wide-range conversion
Fig. 3. (a) Effect on ADC gain error according to the position of parasitic capacitance (b) Overall structure of CDAC
Fig. 2. (a) Differential-Difference Comparator schematic and operation (b) Input referred noise of comparator with different switching
(a)
(b)