## Slide 1
Vswitch
Zin
GND on PCB
<PCB + IC Bump Map>
IC
PCB
Zin
Transmission line
Transmission line
Vswitch
- 120GHz On-Chip Antenna
Design of D-band on-chip antennas and switches
for B5G communication and radar systems
JIMIN YANG, KYUNGBIN YOO, SEHOON PARK
Electronic Engineering, Kyungpook National University
Introduction
Design 1
Design 2
Conclusion
- 140GHz Switch with Packaging Consideration
The importance of D-band frequencies in B5G (Beyond 5G) communications and radar systems is increasing, necessitating designs that minimize loss and parasitic components.
Implementation of a D-band on-chip antenna operating at 120GHz.
Implementation of an IC-PCB co-integration-based switching IC that provides 1-bit impedance control for 140GHz-band RIS (Reconfigurable Intelligent Surface) antennas.
Fig. 2. Simulated Radiation Gain
Fig. 1. Principle of Antenna
Antenna structure utilizing constructive interference.
Patch AMC (Artificial Magnetic Conductor) structure + Backside metal dipole antenna.
Simulated Radiation Gain = 3.19dBi.
Switching IC for 1-bit impedance control of 140GHz band RIS antennas.
Proposed a low-parasitic structure using stud bumps instead of wire bonding, which suffers from difficult parasitic control in IC-PCB co-integration.
Minimizing parasitic effects by utilizing high-performance Top Metals(LB,OI,IA,IB) as Ground layers
Achieved Zin =86.7-14.3j at Vswitch High, Zin =127.3+145.6j at Vswitch Low.
Discrepancies in S11 results due to EM simulations conducted without accurate loss data for 120GHz on-chip silicon materials.
Antenna radiation gain could not be measured due to link budget constraints of the detection equipment.
Measurements are currently on hold as the PCB fabrication for the RIS antenna is not yet complete.
Fig. 3. Chip photo of Antenna
Fig. 6. IC-PCB Co-integration Structure
Fig. 5. Antenna S11 Result
Fig. 4. Antenna Measurement setup
Acknowledgement
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.