## Slide 1
D-band SPST and SPDT Switches in 28-nm CMOS Technology
Songmi Je, Dongkyo Kim
Dong-A University, Dept. of Electronic Engineering
Coupler-based D-band SPST and SPDT switches were implemented in 28-nm CMOS.
The measured results verify the operation of the proposed SPST and SPDT switches.
The simulation-to-measurement discrepancy may be related to the varactor-based reflective load.
Future work will focus on varactor characterization and reflective-load optimization.
A varactor-based reflective load is used to control the load impedance in the proposed switch.
The SPST switch consists of a 90° hybrid coupler and two reflective loads.
By changing the reflective load impedance, the switch state is controlled.
The SPDT switch is implemented by combining two coupler-based SPST paths with complementary control voltages.
D-band switches are essential for phased-array and OOK communication systems.
Low insertion loss, high isolation, and wide bandwidth are required at D-band frequencies.
Coupler-based single-pole single-throw (SPST) and single-pole double-throw (SPDT) switches were implemented in 28-nm CMOS.
Design
Introduction
Conclusion
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Measurement Results
Insertion loss : 4.7–7.6 dB
Isolation : 16.2–22.2 dB
Reflective load circuit
SPST switch schematic
SPDT switch schematic
SPST switch
Insertion loss : 7.3–10.2 dB
Isolation : 18.9–25.3 dB
SPDT switch