## Slide 1
High-Side Current Sensing Interface with Low-Offset
Chopped-CBIA for Battery Management Systems
Introduction
  Battery Management System (BMS) requires accurate bidirectional current sensing to monitor charge and discharge currents over a wide input range. This work presents an current reference (IREF) based high-side current sensing interface. The front-end employs a low-offset chopped-current balanced instrumentation amplifier (CBIA) with programmable gain and targets a ± 50 mV input range, corresponding to ± 50 A under a 1 mΩ shunt resistor. In the proposed sensing concept, the battery current is estimated from the ratio between the battery-current signal and the reference-current tone, so that common gain-related variations can be reduced. The interface is characterized using simulation and measurement results, and the observed linearity degradation is analyzed in terms of input-dependent common-mode variation and CM-to-DM conversion.
Chip Photo and Measurement Setup
Proposed IREF-based High-Side Current Sensor
The chip fabrication and EDA tool were supported by the IC Design Education Center(IDEC), Korea.
Acknowledgement
Pangi Park1, Dabin Hong1 and SeongHwan Cho1
1Department of Electrical Engineering, KAIST, Daejeon, Korea
▲ Chip Die Photo
▲ Measurement Setup
Proposed IREF-based high-side current sensor with input bias generator, chopped-CBIA, and ADC readout.
Off-chip 1 mΩ sense resistor generates a small differential input voltage.
Input bias generator sets the input common-mode voltage near 1.2 V.
Low-Offset Chopped-CBIA
10k
200k
Implemented with TSMC 180nm technology (HM-2501).
Effective area : 2.08 mm2.
Measurement Results
Schematic of chopped-CBIA
Offset Monte Carlo Simulation
For a 1 mΩ sense resistor, 1 μV offset corresponds to about 1 mA current error.
Estimation of IBAT
DC current measurement was performed at the amplifier output.
A 2-point calibration was applied at ± 45 A.
Linearity : ± 0.15 % over ± 50 A
CM-to-DM Conversion Simulation Result (Revision Point)
Input DC current changes the IA input common-mode condition.
CBIA converts this common-mode variation into differential output error.
This CM-to-DM conversion is likely responsible for the input-dependent IREF ton variation.