## Slide 1
A D-band 2-D Phased-Array Transceiver Module using Aperiodic Sub-Array in Fan-Out Wafer-Level Package
Seung-Uk Choi1), Inho Choi1), Jiwon Kang1), Jiseul Kim1) and Ho-Jin Song2) 1)Dept. of Electrical Engineering, POSTECH, Pohang, South Korea 2)Dept. of Electrical Engineering and Graduate School of Semiconductor Technology, POSTECH, Pohang, South Korea
Abstract
A D-band 16-channel two-dimensional (2-D) phased-array transceiver module implemented in a fan-out wafer-level package (FOWLP) is presented. The module integrates four 28-nm CMOS transceivers with a Beatty-based aperiodic silicon resonator antenna (SRA) array to suppress grating lobes. The system performance is evaluated through over-the-air (OTA) measurements, achieving a peak EIRP of 20 dBm and data rates up to 32 Gb/s.
Introduction
- D-band (110-170 GHz) communication has gained considerable attention as a solution for next-generation high-throughput wireless systems due to its vast spectrum availability.
- Realizing 2-D phased-array modules in D-band have several challenges. First, high parasitic and interconnection losses. Second, hard to make 2-D beamforming module constrained by the size mismatch between D-band transceiver die and λ/2-antenna grid.
- Fan-Out Wafer-Level Packaging (FOWLP) is promising package solution for sub-THz phased-array design utilizing bumpless interconnections and high resolution metallic environment. [1]
Aperiodic sub-array configuration
 In this poster, a D-band 2-D 16-channel phased-array TRX module with an aperiodic sub-array configuration in FOWLP package is presented
FOWLP Module Design and Measurement
Reference [1] Bahrami, Sirous, et al. "A D-Band Phased Array Transmitter With Silicon-Based Resonator Antennas Using FOWLP Technology." IEEE Transactions on Microwave Theory and Techniques (2025).
Acknowlegement Chip fabrication was supported by the IC Design Education Center. this work was supported by the National Research Foundation of Korea (NRF) grant funded by the Korea government (MSIT) (No. RS-2024-00334214), and the EDA tool was supported by IC Design Education Center (IDEC), Korea.
  A D-band 16-channel 2-D phased-array transceiver module is successfully implemented using a 28-nm CMOS process and FOWLP technology.
  The proposed Beatty-based aperiodic sub-array configuration effectively suppresses spatial aliasing, enabling reliable 2-D beam steering without severe grating lobes.
  The integrated dual-port SRAs function as both radiating elements and structural fillers, achieving both excellent OTA performance and thermo-mechanical stability.
  The module achieves a peak EIRP of 20 dBm and supports high-speed data transmission up to 32 Gb/s, demonstrating its strong potential for next-generation sub-THz wireless systems.
Fig. 1. Design challenges of D-band (140 GHz) phased-array transceiver module
x
z
Periodic Sub-array
x
z
: Phase Center
: Element Antenna
: Sub-Array Group
d
2d
d
3d
2.5d
2d
Aperiodic Sub-array
(a)
(b)
Fig. 2. (a) Diagram of periodic array with 2-element sub-arrays, and an aperiodic sub-array with 2- and 3-element (b) Simulated radiation patterns of the 30-element array
 The uniform periodic sub-array inherently suffers from spatial aliasing, resulting in high-level grating lobes.
 By mixing 2- and 3-element groups to create variable phase center spacings, the aperiodic configuration effectively prevents coherent signal addition at grating lobe angles and flattens them into a spatial noise floor.
Fig. 3. Aperiodic sub-array antenna configuration
in FOWLP module for TX (left) and RX (right)
The 11x12 antenna grid is grouped into aperiodic sub-arrays for each four 4TX/4RX CMOS dies.
Each TX and RX sub-array is mapped to form a sparse array.
The beamforming performance are verified by simulation.
CMOS Transceiver Design
Vector-sum Phase-Shifter
TRX Block diagram and Die-photo
Inj.-locked Freq. Multiplier
(with Mixer)
 The D-band 4-channel transceiver is fabricated in a 28-nm bulk LP CMOS process. RF phase-shifting architecture is applied.
 Neutralized TF-based PA, Catesian vector-sum PS, ILFM is employed.
Conclusion
 Dual-port silicon-based resonator antennas (SRAs) are integrated within the 14.76 mm × 16.2 mm FOWLP module, acting as both radiating elements and dielectric fillers to mitigate substrate warpage.
 Over-the-air (OTA) measurements demonstrate successful 2-D beam steering within a ±10° range in both azimuth and elevation planes with well-suppressed grating lobes