## Slide 1
2026 IDEC Congress CDC
ADPLL-based FM Modulator Using Two-Point Modulation
Solmon Shin, Youngsik Kim, and Shinwoong Kim
Department of Computer and Electronic Engineering,
Handong Global University, Pohang, Korea
Introduction
Calibration Techniques
System Architecture
Conclusion
[https://article.murata.com/ko-kr/article/basics-of-wireless-communication-1]
<Conventional Digital PLL>
<DPLL using Two-point modulation>
The modulation bandwidth is fundamentally limited by the loop bandwidth
To overcome this limitation, two-point modulation is employed
In addition, background calibration of TDC non-linearity is applied within the PLL loop to enhance modulation accuracy
ADPLL-based FM Modulators are essential for wireless systems
The proposed ADPLL-based FM Modulator employs:
Fractional-N PLL using DSM
Two-point FM Modulation
ADC-assisted coarse-to-fine TDC
In-loop background TDC Nonlinearity calibration
[N. Marculic, 16’JSSC]
(b)
TDC Gain Calibration for DSM Quantization Noise Cancellation
DSM quantization error (QE) propagates to the TDC output and degrades linearity
The TDC gain is calibrated using sign-sign LMS based on QE
Two-Point Modulation Gain Calibration
Mismatch between slow path and fast path introduces modulation distortion
Sign-sign LMS is employed to align the modulation gains
The calibration compensates delay and gain mismatch between the two paths
Tx_DATA
DCTRL
DCO
Frequency
Figure 1. Block diagram of the proposed ADPLL
Figure 3. (a) TDC gain calibration for DSM quantization noise cancellation, (b) Two-point modulation gain calibration
(a)
Figure 4. Simulated FM modulation with 1 Mbps TX data (1MHz frequency deviation).
FM Modulator
Figure 5. Simulated Phase noise spectrum
Figure 6. Layout view
Technology(nm) | 28
PLL Architecture | ADPLL
Oscillator Type | Ring DCO
Output Frequency | 4.8 GHz
FSK Modulation | Two-Point
Calibration Type | Background
In-Band Noise (dBc/Hz) | -102.5 @1 MHz
RMS Jitter (ps) | 5
Date Rate (Mb/s) | 1
Frequency Deviation | 1MHz
TDC INL (Before) | 10 LSB
TDC INL (After) | 5 LSB
Core Area (mm2) | 0.5
Technology(nm) | 28
PLL Architecture | ADPLL
Oscillator Type | Ring DCO
Output Frequency | 4.8 GHz
FSK Modulation | Two-Point
Calibration Type | Background
In-Band Noise (dBc/Hz) | -102.5 @1 MHz
RMS Jitter (ps) | 5
Date Rate (Mb/s) | 1
Frequency Deviation | 
TDC INL (Before) | 10 LSB
TDC INL (After) | 5 LSB
Core Area (mm2) | 0.5
The proposed ADPLL achieves accurate FM modulation using Two-point modulation and In-loop TDC Non-Linearity Calibration
Table 1. Performance summary
Figure 2. Two-point modulation architecture
Fast path directly modulates the DCO
Slow path processes low-frequency components through the PLL loop
This architecture overcomes the modulation bandwidth limitation of PLLs